（ As technology continues to update, we retain the right to change technology design. ）

Catalogue

1. Products introduction	2

2. Technical parameter	2

3. Characteristics of Structural	2

4. Operate and Maintenance	3

5. Installation	3

6. Maintenance and Repair	3

7. Electrical Schematic	4

- Products introduction

This machine is used to mix the different powder material. Making used of blades to rotate in material trough, it can mix the different materials evenly and uniformly. The reverse operation of material trough and blades makes the materials mixing more evenly and uniformly. This machine is also suitable for mixing different mainly complementing the material such industrial departments as chemical industry, food, etc. It is most suitable for mixing semi-solidly, solution or gluing and spending big material.

- Technical parameter

| Model | CH--10 |
| --- | --- |
| Trough capacity（kg） | 10 |
| Spindle speed (r/min) | 24 |
| Mixing cycle（min） | 5-20 |
| Main motor (kw) | 0.25 |
| Dumping motor (kw) | by hand |
| Net weight (kg) | 40 |
| Overall size(mm) | 600*280*450 |

# Characteristics of Structural

The machine is an integer seat; it is flexible and steady mixing thick liquid. The parts that contracted with material are made of stainless steel. Have a good corrosion resistance, which can guarantee the quality of mixed materials, so that the materials don't be polluted and changed color.

Transmission mechanism mainly driven by the worm wheel drive and worm drive, low noise and have enough lubrication. So the machine has good lubrication condition, which will improve the service life of machine.

This machine inverted material by hand, it is easy to operate.

- Operate and Maintenance

4.1.Try to test the machine before you use the machine, and should check the fastening level of all the connected pieces of machine, check the lubrication amount of reducer and the integrity of electrical equipment, then turn off the main power, test the machine. Separately press the inching discharging button, reset button, check if there working situation, after meeting the above requirements, you can use the machine. (Please note that the discharging button and reset button can not be pressed at the same time.)

4.2. Covering the trough cover after feed materials; avoid the materials overflow the trough. The cover is made of plexiglass so that we can observe the situation of mixing. If it achieved the desired effect, we can start to feed by press the feeding buttons. When the hopper is near the machine seat, you should stop feeding in order to avoid damaging the machine. After feeding, press the reset button, make the feeding trough back to the original position.

- Installation

The machine is packed in wooden case, after demolished wooden, just move to the appropriate place, then connect the power so that you can use it.

- Maintenance and Repair

6.1. If you often use the reducer, you should replace oil once every three months. And you should clean the reducer before you replace the oil.

6.2.The place between stirring gear bearing cap side with the shaft and blade, and the axis is equipped with oil cup lubrication. Add butter in butter gun every work-shift.

6.3. Regularly check the mechanical one-two times every month, check the worm, worm gear, bearing, seals, etc., make sure if the machine operate flexibly and if the fasteners are loosen, if you found abnormal situation, please deal with it timely.

6.4.When the machine running, if found abnormal vibration or abnormal sound, should immediately stop machine and check it.

6.5.Electrical control components should be kept clean and sensitive, if found the failure, should repaired it promptly.

6.6.When assembly and disassembly the stirring slurry, which should be light demolition, stable equipment and light placed so as to avoid deformation and damage.

6.7.After the use of machine, please clean out the residual material of all parts. If long time no to use the machine, please clean the whole machine, the surface of machine parts should be coated with anti-rust oil, then cover with tarpaulins.

- Electrical Schematic

# Text boxes

Operation Manual

CH-10  Trough-type Mixer