#### Instruction Manual

#### FS Series

Note: Owner/Operator must read and understand this instruction manual                before using the lift table.

RevB: 04/2010

## Operation and Service Manual

BEFORE OPERATING THE LIFT TABLE, READ THIS MANUAL CAREFULLY AND UNDERSTAND COMPLETELY. KEEP THIS MANUAL ON FILE FOR FUTURE REFERENCE. IF THIS IS LOST, PLEASE CONTACT YOUR LOCAL SUPPLIER FOR A NEW COPY. ALSO, IF THE WARNING/CAUTION DECAL ON THE UNIT IS LOST, PLEASE CONTACT YOUR LOCAL SUPPLIER FOR A NEW DECAL.

NOTE: On this manual, WARNING means the danger which can lead to death or serious injury. CAUTION means the danger which can lead to slight injury or property damage.

- WARNING

1.DO NOT put foot or hand in scissors mechanism.

2.DO NOT allow other person to stand in front of or behind lift table when it is moving.

3.DO NOT move lift table when table is in raised position. Load could fall down.

4.DO NOT enter under table.

5.DO NOT overload lift table.

6.DO NOT put foot in front of rolling wheels. Injury could result.

7.WATCH difference and hardness of floor level when moving lift table. Load could fall down.

8.DO NOT use lift table on slope or inclined surface, lift table may become uncontrollable and create danger.

9.DO NOT lift people. People could fall down and suffer severe injury.

- CAUTION

1.Read this operation manual carefully and understand completely operating lift table. Improper operation could create danger.

2.This lift table is a movable lifter designed to lift or lower rated load on table. NO NOT use lift table for other purpose than its intended use.

3.DO NOT allow person to operate lift table who does not understand its operation.

4.DO NOT lower table too fast. Load could fall down and create danger.

5.KEEP watching the condition of load. Stop operating lift table if load becomes unstable.

6.Byake lift table when sliding load on of off table.

7.DO NOT side or end load. Load must be distributed on at least 80%of table area.

8.DO NOT use lift table with unstable, unbalanced loosely stacked load.

9.Practice maintenance work according to service instructions.

10. DO NOT modify lift table without manufacturer’s written consent.

11. REMOVE load from table and use safety stopper to prevent table from lowering when servicing lift table.

12. This lift table is not designed to be water resistant. Use lift table under dry condition.

- DAILY INSPECTION

Daily inspection is effective to find the malfunction or fault on lift table. Check lift table on the following points before operation.

CAUTION

DO NOT use lift table if any malfunction or fault is found.

- Check for scratch, bending or cracking on the lift table.

- Check if there is any oil leakage from the cylinder.

- Check the vertical creep of the table.

- Check the smooth movement of the wheel.

- Check the function of brake.

- Check if all the bolt and nuts are tightened firmly.

- OPERATING LIFTTABLE

4-1. How to use the brake.

CAUTION

Brake lift table when not moving it in order to prevent sudden movement.

The brake is equipped with the swivel caster on the right side.

- Braking the wheel, press the brake pedal.

- Releasing the brake, lift up the brake pedal.

4-2 Lifting the table

WARNING

DO NOT overload lift table, stay within its rated capacity. DO NOT side end load must be distributed on at least 80% of table area.

Press the lifting pedal several times the until the table reaches the desired position.

The table does not elevate after reaching the highest position even if the lifting pedal is pressed.

The table lowers slightly after reaching the highest position.

| FS20 | FS36 | FS45 | FS46 | FS68 | FS91 |
| --- | --- | --- | --- | --- | --- |
| 200KG | 360KG | 450KG | 460KG | 680KG | 910Kg |

NOTE: The hydraulic cylinder is designed to hold table. As is the nature of the hydraulic system, table lowers very slowly over and extended period of time, Please note the table does not stay at the same position ionindefiinitely.

4-3. Lowering table

WARNING

DO NOT put foot or hand in scissors mechanism.

Pull the lowering down and table lowers.

- Specifications

| Model | Capacity (kg) | Table (mm) | Table Height(mm) | L×W×H (mm) | Pedal to top. (approx. times) | Wheel (mm) φ | Weight (kg) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FS20 | 200 | 700×450 | 260-750 | 1240×450×1010 | 18 | 100 | 48 |
| FS36 | 360 | 920x520 | 410-1350 | 1125×520×1070 | 58 | 125 | 105 |
| FS45 | 450 | 852x502 | 390-910 | 1050×570×1100 | 30 | 125 | 78 |
| FS46 | 460 | 1600x800 | 370-1000 | 1822×800×1100 | 56 | 125 | 140 |
| FS68 | 680 | 1220x610 | 470-1500 | 1445×610×1135 | 40/70 | 150 | 168 |
| FS91 | 910 | 1010×520 | 442-1000 | 1260×540×1100 | 68 | 150 | 112 |

- Service instruction

6.1-1. Lubricate each point described below every month:

6.2.Change hydraulic oil every 12 months.

Lubricating Points

- Fitting of cylinder……Oil

- Roller friction surface……Grease

- Link Pin ……Oil

- Pedal fitting point……Oil

- Link center pin……Oil

- Joint……Grease

- Grease nipple……Grease

- Hydraulic circuit

- Hydraulic Circuit

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Table pair | 1 | 43 | Reservior | 1 |
| 2. | Guide roller | 4 | 44 | O-ring d10×2.65 | 1 |
| 3 | Scissors | 1 | 45 | Filler screw | 1 |
| 4 | Snap ring | 6 | 46 | Washer for reservior | 1 |
| 5 | Link pin | 4 | 47 | Steel ball 5 | 1 |
| 6 | Safety pin | 1 | 48 | Spring base | 1 |
| 7 | Hex bolt | 16 | 49 | Regulating pressure spring | 1 |
| 8 | Washer | 18 | 50 | Regulating pressure screw | 1 |
| 9 | Frame pair | 1 | 51 | O-ring d7.1×1.8 | 1 |
| 10 | Front wheel | 2 | 52 | End cover | 1 |
| 11 | Spring washer | 19 | 53 | O-ring d15×2.65 | 2 |
| 12 | Hex. nut | 18 | 54 | Regulating speed spring | 1 |
| 13 | Rear wheel | 2 | 55 | Regulating speed slide valve | 1 |
| 14 | Handle pin | 4 | 56 | Regulating speed spring casing | 1 |
| 15 | Handle lock spring L | 1 | 57 | Regulating speed valve casing | 1 |
| 15A | Handle lock spring R | 1 | 58 | Steel ball 7 | 1 |
| 16 | Bushing | 2 | 59 | O-ring d6.9×1.8 | 1 |
| 17 | Snap ring | 4 | 60 | Conical valve | 1 |
| 18 | Lock bar | 1 | 61 | Check valve spring | 1 |
| 19 | Put pressure assembly line | 1 | 62 | Check valve casing | 1 |
| 20 | Screw M6×30 | 1 | 63 | O-ring d10×1.8 | 1 |
| 21 | Spring pin | 1 | 64 | Check valve screw | 1 |
| 22 | Control link | 1 | 65 | Spring base | 1 |
| 23 | Handle | 1 | 66 | Spring | 1 |
| 24 | Cover-type nut M6 | 1 | 67 | Seal cover d18×D25×4.5 | 1 |
| 25 | Split pin | 1 | 68 | O-ring d18×2.65 | 1 |
| 26 | Pin | 1 | 69 | Pump plunger | 1 |
| 27 | Pin axle | 1 | 70 | Y-ring | 1 |
| 28 | Retainer 16 | 9 | 71 | Pump body for plunger | 1 |
| 29 | Seal cover d30×D42×7 | 1 | 72 | O-ring d28×3.1 | 1 |
| 30 | Cylinder cover | 1 | 73 | Pump body | 1 |
| 31 | O-ring d63×2.65 | 2 | 74 | O-ring d10.6×2.65 | 1 |
| 32 | O-ring d30×3.55 | 1 | 75 | Spring | 1 |
| 33 | Piston rod | 1 | 76 | Reflux rod | 1 |
| 34 | Spacing casing | 1 | 77 | O-ring d4×1.8 | 1 |
| 35 | Guide ringδ1.5×15 | 1 | 78 | Guide casing | 1 |
| 36 | O-ring D20×2.4 | 1 | 79 | Protect casing | 1 |
| 37 | Seal ring d34×D40×4.5 | 1 | 80 | Lever | 1 |
| 38 | Piston rod retainer | 1 | 81 | Lever bushing | 1 |
| 39 | Retaining ring 18 | 1 | 82 | Washer 6 | 2 |
| 40 | Piston | 1 | 83 | Spring washer 6 | 2 |
| 41 | Cylinder | 1 | 84 | Hex soch screw M6×16 | 1 |
| 42 | Cylinder washer | 1 |  |  |  |
| A | Pump ass’y | 29-84 |
| B | Swivel wheel ass’y | 13 |
| C | Front wheel ass’y | 10 |
| D | Sealkit ass’y | 29,31,32,35,36,37,44,51, 53,59,63,57,68,70,72,74,77 |
| E | Handle ass’y | 19-26,83,84 |

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d30×D42×7 | 1 | 61 | Control link | 1 |
| 2. | Cylinder cover | 1 | 62 | Handle | 1 |
| 3. | O-ring d63×2.65 | 2 | 63 | Cover type nut M6 | 1 |
| 4. | O-ring d30×3.55 | 1 | 64 | Spacing casing | 2 |
| 5. | Piston Rod | 1 | 65 | Spring washer 12 | 2 |
| 6. | Spacing casing | 1 | 66 | Hex screw M12×30 | 2 |
| 7. | Guide ring δ1.5×15 | 1 | 67 | Split pin 2×15 | 1 |
| 8. | O-ring D20×2.4 | 1 | 68 | Pin | 1 |
| 9. | Seal ring d34×D40×4.5 | 1 | 72 | Pedal bent pipe | 1 |
| 10. | Retainer for piston rod | 1 | 73 | Hex sock screw M8×20 | 2 |
| 11. | Spacing retainer 18 | 1 | 74 | Shake link | 1 |
| 12. | Piston | 1 | 75 | Spring | 2 |
| 13. | Cylinder | 1 | 76 | Retainer 10 | 2 |
| 14. | Washer for cylinder | 1 | 77 | Pin axle | 2 |
| 15. | Reservoir | 1 | 78 | Link | 2 |
| 16. | O-ring d10×2.65 | 1 | 79 | Nut M8 | 16 |
| 17. | Filler screw | 1 | 80 | Spring washer 8 | 16 |
| 18. | Washer for reservoir | 1 | 81 | Washer 8 | 34 |
| 19. | Steel ball 5 | 1 | 82 | Wheel | 2 |
| 20. | Spring base | 1 | 83 | Hex sock screw M8×25 | 16 |
| 21. | Regulating pressure spring | 1 | 84 | Wheel | 2 |
| 22. | Regulating pressure screw | 1 | 85 | Pin axle | 1 |
| 23. | O-ring d7.1×1.8 | 1 | 86 | Retaining ring for axle 20 | 7 |
| 24. | End cover | 1 | 87 | Chassis | 1 |
| 25. | O-ring d15×2.65 | 2 | 88 | Bolt M6×8 | 1 |
| 26. | Regulating slide-valve | 1 | 89 | Pin axle for chassis | 1 |
| 27. | Regulating speed spring | 1 | 90 | Bushing | 4 |
| 28. | Regulating speed spring casing | 1 | 91 | Locking nut M16x1.5 | 6 |
| 29. | Regulating speed slide-casing | 1 | 92 | Washer 16 | 6 |
| 30. | Steel ball 7 | 1 | 93 | Pin axle | 2 |
| 31. | O-ring d6.9×1.8 | 1 | 94 | Bushing 2010 | 4 |
| 32. | Check valve casing | 1 | 95 | Bushing 2040 | 4 |
| 33. | Conical valve | 1 | 96 | Retaining ring for axle 16 | 2 |
| 34. | Spring | 1 | 97 | Pin axle | 1 |
| 35. | O-ring d10×1.8 | 1 | 98 | Hex socket set screw M8×12 | 1 |
| 36. | Check valve screw | 1 | 99 | Oil cup | 1 |
| 37. | Seal cover d18×D25×4.5 | 1 | 100 | External scissors lever for table | 1 |
| 38. | O-ring d18×2.65 | 1 | 101 | Internal scissors lever for table | 1 |
| 39. | Pump plunger | 1 | 102 | Roller for table | 2 |
| 40. | Y-ring d10×D18×6 | 1 | 103 | Table | 1 |
| 41. | Pump body for plunger | 1 | 104 | Spring pin 8×30 | 2 |
| 42. | O-ring D28×3.1 | 1 | 105 | Screw bolt M10×40 | 2 |
| 43. | Pump body | 1 | 106 | Washer 10 | 4 |
| 44. | O-ring d10.6×2.65 | 1 | 107 | Safety rod | 2 |
| 45. | Spring | 1 | 108 | Locking nut M10 | 2 |
| 46. | Reflux rod | 1 | 109 | External scissors lever for chassis | 1 |
| 47. | O-ring d4×1.8 | 1 | 110 | Internal scissors lever for chassis | 1 |
| 48. | Guide casing | 1 | 111 | Bushing | 2 |
| 49. | Protect casing | 1 | 112 | Roller for chassis | 2 |
| 50. | Lever | 1 | 113 | Washing | 2 |
| 51. | Lever bushing | 1 | 114 | Pin axle | 2 |
| 52. | Washer 6 | 2 | 115 | Hex screw M8×16 | 2 |
| 53. | Spring washer 6 | 2 | 116 | Locking nut M14 | 2 |
| 54. | Hex sock screw M6×16 | 1 | 117 | Washer 14 | 2 |
| 55 | Put pressure assembly line | 1 | 118 | Pin axle | 1 |
| 58 | Washer 8 | 2 | 119 | Bushing 1610 | 2 |
| 59 | Screw M6×30 | 1 | 120 | Bushing 1620 | 4 |
| 60. | Spring pin 5×14 | 1 |  |  |  |
| A | Pump ass’y | 1～49 |
| B | Swivel wheel ass’y | 82 |
| C | Front wheel ass’y | 84 |
| D | Sealkit ass’y | 1,3, 4,7,8,9,16,23,25,31,35,37,38,40,42,44,47 |
| E | Handle ass’y | 52,53,55,59,60,61,62,63,67,68 |

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d30×D42×7 | 1 | 55 | Hex sock screw M6×16 | 1 |
| 2. | Cylinder cover | 1 | 56 | Put pressure assembly line | 1 |
| 3. | O-ring d63×2.65 | 2 | 57 | Steel wire | 1 |
| 4. | O-ring d30×3.55 | 1 | 58 | Nut M8 | 6 |
| 5. | Piston Rod | 1 | 59 | Washer 8 | 6 |
| 6. | Spacing casing | 1 | 60. | Screw M6×30 | 1 |
| 7. | Guide ring δ1.5×15 | 1 | 61 | Spring pin 5×14 | 1 |
| 8. | O-ring D20×2.4 | 1 | 62 | Spring pin 5×14 | 1 |
| 9. | Seal ring d34×D40×4.5 | 1 | 63 | Control link | 1 |
| 10. | Retainer for piston rod | 1 | 64 | Handle | 1 |
| 11. | Spacing retainer 18 | 1 | 65 | Spring washer 12 | 2 |
| 12. | Piston | 1 | 66 | Hex screw M12×30 | 2 |
| 13. | Cylinder | 1 | 67 | Split pin 2×15 | 1 |
| 14. | Washer for cylinder | 1 | 68 | Pin | 1 |
| 15. | Reservoir | 1 | 69 | U- fork | 1 |
| 16. | O-ring d10×2.65 | 1 | 70 | Nut M6 | 1 |
| 17. | Filler screw | 1 | 71 | Bolt | 1 |
| 18. | Washer for reservoir | 1 | 72 | Pedal bent pipe | 1 |
| 19. | Steel ball 5 | 1 | 73 | Hex sock screw M8×20 | 2 |
| 20. | Spring base | 1 | 74 | Shake link | 1 |
| 21. | Regulating pressure spring | 1 | 75 | Spring | 2 |
| 22. | Regulating pressure screw | 1 | 76 | Retainer 10 | 2 |
| 23. | O-ring d7.1×1.8 | 1 | 77 | Pin axle | 2 |
| 24. | End cover | 1 | 78 | Link | 2 |
| 25. | O-ring d15×2.65 | 2 | 79 | Nut M10 | 16 |
| 26. | Regulating slide-valve | 1 | 80 | Spring washer 10 | 16 |
| 27. | Regulating speed spring | 1 | 81 | Washer 10 | 36 |
| 28. | Regulating speed spring casing | 1 | 82 | Wheel | 2 |
| 29. | Regulating speed slide-casing | 1 | 83 | Hex sock screw M10×25 | 16 |
| 30. | Steel ball 7 | 1 | 84 | Wheel | 2 |
| 31. | O-ring d6.9×1.8 | 1 | 85 | Pin axle | 1 |
| 32. | Check valve casing | 1 | 86 | Retaining ring for axle 20 | 7 |
| 33. | Conical valve | 1 | 87 | Chassis | 1 |
| 34. | Spring | 1 | 88 | Bolt M6×8 | 1 |
| 35. | O-ring d10×1.8 | 1 | 89 | Pin axle for chassis | 1 |
| 36. | Check valve screw | 1 | 90 | Bushing | 4 |
| 37. | Seal cover d18×D25×4.5 | 1 | 91 | Locking nut M14 | 6 |
| 38. | O-ring d18×2.65 | 1 | 92 | Washer 14 | 6 |
| 39. | Pump plunger | 1 | 93 | Washer 16 | 6 |
| 40. | Y-ring d10×D18×6 | 1 | 94 | Pin axle | 3 |
| 41. | Pump body for plunger | 1 | 95 | Bushing 1612 | 8 |
| 42. | O-ring D28×3.1 | 1 | 96 | Bushing 1620 | 6 |
| 43. | Pump body | 1 | 97 | Retaining ring for axle 16 | 8 |
| 44. | O-ring d10.6×2.65 | 1 | 98 | Roller for chassis | 2 |
| 45. | Spring | 1 | 99 | Bushing | 2 |
| 46. | Reflux rod | 1 | 100 | Locking nut M10 | 2 |
| 47. | O-ring d4×1.8 | 1 | 101 | Washer 10 | 4 |
| 48. | Guide casing | 1 | 102 | Safety rod | 2 |
| 49. | Protect casing | 1 | 103 | Screw bolt M10×40 | 2 |
| 50. | Lever | 1 | 104 | Spring pin 8×30 | 2 |
| 51. | Lever bushing | 1 | 105 | Hex socket set screw M8×12 | 1 |
| 52. | Cover type nut M6 | 1 | 106 | Roller for table | 2 |
| 53. | Washer 6 | 2 | 107 | Table | 1 |
| 54. | Spring washer 6 | 2 |  |  |  |
| A | Pump ass’y | 1～49 |
| B | Swivel wheel ass’y | 82 |
| C | Front wheel ass’y | 84 |
| D | Sealkit ass’y | 1,3, 4,7,8,9,16,23,25,31,35,37,38,40,42,44,47 |
| E | Handle ass’y | 52,53,55,59,60,61,62,63,67,68 |

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Chassis | 1 | 42 | Wire retainer 30 | 1 |
| 2. | Rear wheel | 2 | 43 | Guideing δ2×19.8 | 1 |
| 3. | Washer 10 | 16 | 44 | O-ring d55×2.65 | 1 |
| 4. | Spring washer 10 | 16 | 45 | Cylinder cover | 1 |
| 5. | Nut M10 | 16 | 46 | Retaining ring for axle 55 | 1 |
| 6. | Hex soch screw M10x25 | 16 | 47 | Seal cover d30×D40×7 | 1 |
| 7. | Front wheel | 2 | 48 | Wire retainer 60 | 1 |
| 8. | Washer 8 | 3 | 49 | Piston rod | 1 |
| 9. | Spring washer 8 | 11 | 50 | Oil cup M6 | 7 |
| 10. | Spring washer M8x16 | 1 | 51 | Bearing GE30ZS | 1 |
| 11. | High pressure joint | 2 | 52 | Piston head pin | 1 |
| 12. | Seal ring d10.37×D15.88×2.03 | 5 | 53 | Spring washer M8x12 | 2 |
| 13. | Tubing joint | 2 | 54 | Nut M14 | 2 |
| 14. | Suction pipe d8×D12 | 1 | 55 | Washer 14 | 2 |
| 15. | Spring washer M8x40 | 2 | 56 | Spacer | 2 |
| 16. | Storage tank | 1 | 57 | Bumper | 2 |
| 17. | Cushion tube | 2 | 58 | External scissors lever for chassis | 1 |
| 18. | Oil pump assembly | 1 | 59 | Retaining ring for axle 20 | 6 |
| 19. | Limit bracket | 1 | 60 | Roller for chassis | 2 |
| 20. | Return spring | 1 | 61 | Bushing | 2 |
| 21. | Spring washer 6 | 3 | 62 | Bushing 3025 | 1 |
| 22. | Hex soch screw M6x40 | 2 | 63 | Cylinder pin | 1 |
| 23. | Seal ring d16.51×D25.4×2.03 | 5 | 64 | Washer | 6 |
| 24. | High pressure hose | 1 | 65 | Nut M16x1.5 | 6 |
| 25. | Pipe joint | 2 | 66 | Scissor shaft bushing | 4 |
| 26. | Pedal cover | 1 | 67 | Scissor shaft | 4 |
| 27. | Lever | 1 | 68 | Hex soch screw M8×20 | 6 |
| 28. | Hex soch screw M6x16 | 1 | 69 | Pin axle | 1 |
| 29. | Large washer 6 (D18×d6.4×1.6) | 1 | 70 | Internal scissors lever for chassis | 1 |
| 30. | Bushing | 1 | 71 | Hex soch screw M14×45 | 2 |
| 31. | Armrest washer | 2 | 72 | pin | 2 |
| 32. | Spring washer 12 | 2 | 73 | Bushing | 6 |
| 33. | Hex screw M12×30 | 2 | 74 | Internal scissors lever for table | 1 |
| 34. | Handle | 1 | 75 | Roller for table | 2 |
| 35 | Explosion proof joint | 1 | 76 | Bushing | 2 |
| 36. | Seal ring 14 | 1 | 77 | Pin axle | 1 |
| 37. | Spring | 1 | 78 | Bushing | 2 |
| 38. | Explosion proof valve core | 1 | 79 | External scissors lever for table | 1 |
| 39. | Cylinder | 1 | 80 | Table | 1 |
| 40. | Piston | 1 | 81 | Bolt M6×12 | 1 |
| 41. | Bidirectional Seal Ring d44xD60x18.4 | 1 |  |  |  |

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 85. | Valve seat | 1 | 113 | O-ring D28×2.4 | 1 |
| 86. | Spring pin 5×18 | 1 | 114. | Retaining ring | 1 |
| 87 | Steel ball 6.5 | 1 | 115 | Pump body for plunger | 1 |
| 88 | O-ring d10×1.8 | 2 | 116 | Seal cover d20×D28×5 | 1 |
| 89 | Guide casing | 1 | 117 | Seal cover d20×D28×4.5 | 1 |
| 90 | Spring | 1 | 118 | Return spring | 1 |
| 91. | O-ring d7.1×1.8 | 1 | 119 | Spring seat | 1 |
| 92. | Reflux rod | 1 | 120 | Spring guard | 1 |
| 93 | Plug-governor valve | 1 | 121 | Pin | 1 |
| 94 | Seal ring d16.7×D24×1.5 | 1 | 122 | Bushing 10120 | 2 |
| 95. | Screw | 1 | 123 | Spacer sleeve | 2 |
| 96 | Plastic head | 1 | 124 | Link | 1 |
| 97. | Regulating speed slide-casing | 1 | 125 | Roller | 1 |
| 98. | Regulating speed spring casing | 1 | 126 | Wire retainer 10 | 1 |
| 99. | Speed regulating valve element | 1 | 127 | Pedal cover | 1 |
| 100. | Wire retainer 8 | 1 | 128 | Split pin 3.2×20 | 1 |
| 101 | Nylon pad | 1 | 129 | Pin axle | 1 |
| 102 | O-ring d33.5×2.65 | 1 | 130 | Steel ball 8 | 1 |
| 103. | Washer | 1 | 131 | Check valve | 1 |
| 104 | Screw plug | 1 | 132 | Spring | 1 |
| 105 | Spring pin 2.5×8 | 1 | 133 | Seal ring d12.7×D19×1.5 | 1 |
| 106 | Spring seat | 1 | 134 | Check valve screw | 1 |
| 107 | Steel ball 6 | 1 | 135 | Check valve screw | 1 |
| 108 | Large spring | 1 | 136 | Bolt M10×1×6 | 1 |
| 109 | Small spring | 2 | 137 | Regulating pressure spring | 1 |
| 110 | Steel ball 4 | 2 | 138 | Spring base | 1 |
| 111 | Pump body | 1 | 139 | Steel ball 5 | 1 |
| 112 | Spring pin 5×26 | 1 |  |  |  |

| NO. | DESCRIPTION | Qty | NO. | DESCRIPTION | Qty |
| --- | --- | --- | --- | --- | --- |
| 1. | Seal cover d30×D42×7 | 1 | 54. | Hex soch screw M6×16 | 1 |
| 2. | Cylinder cover | 1 | 55. | Put pressure assembly line | 1 |
| 3. | O-ring d63×2.65 | 2 | 56. | Washer 8 | 2 |
| 4. | O-ring d30×3.55 | 1 | 57 | Spring pin 5×14 | 1 |
| 5. | Piston Rod | 1 | 58. | Control link | 1 |
| 6. | Spacing casing | 1 | 59. | Handle | 1 |
| 7. | Guidering δ1.5×15 | 1 | 60. | Spacing casing | 2 |
| 8. | O-ring D20×2.4 | 1 | 61. | Spring washer 12 | 2 |
| 9. | Seal ring d34×D40×4.5 | 1 | 62. | Hex screw M12×30 | 2 |
| 10. | Retainer for piston rod | 1 | 63. | Split pin 2×15 | 1 |
| 11. | Spacing retainer 18 | 1 | 64. | Pin | 1 |
| 12. | Piston | 1 | 65 | Pedal bent pipe | 1 |
| 13. | Cylinder | 1 | 66. | Hex soch screw M8×20 | 2 |
| 14. | Washer for cylinder | 1 | 67. | Shake link | 1 |
| 15. | Reservior | 1 | 68. | Spring | 2 |
| 16. | O-ring d10×2.65 | 1 | 69. | Retainer 10 | 2 |
| 17. | Filler screw | 1 | 70. | Pin axle | 2 |
| 18. | Washer for reservior | 1 | 71. | Link | 2 |
| 19. | Steel ball 5 | 1 | 72. | Wheel | 2 |
| 20. | Spring base | 1 | 73. | Nut M10 | 16 |
| 21. | Regulating pressure spring | 1 | 74. | Spring washer 10 | 16 |
| 22. | Regulating pressure screw | 1 | 75. | Washer 10 | 36 |
| 23. | O-ring d7.1×1.8 | 1 | 76. | Hex soch screw M10×25 | 16 |
| 24. | End cover | 1 | 77. | Wheel | 2 |
| 25. | O-ring d15×2.65 | 2 | 78. | axle | 1 |
| 26. | Regulating speed spring | 1 | 79. | Retainer 20 | 7 |
| 27. | Regulating slide-valve | 1 | 80. | Chassis | 1 |
| 28. | Regulating speed spring casing | 1 | 81. | Table | 1 |
| 29. | Regulating speed slide-casing | 1 | 82. | Roller for table | 2 |
| 30. | Steel ball 7 | 1 | 83. | Bushing | 2 |
| 31. | O-ring d6.9×1.8 | 1 | 84. | Split pin 3.2×26 | 1 |
| 32. | Conical valve | 1 | 85. | Nut M16 | 1 |
| 33. | Spring | 1 | 86. | Washing | 1 |
| 34. | Check valve casing | 1 | 87. | Bushing | 4 |
| 35. | O-ring d10×1.8 | 1 | 88. | Spring pin 8×30 | 2 |
| 36. | Check valve screw | 1 | 89. | Screw bolt M10×40 | 2 |
| 37. | Seal cover d18×D25×4.5 | 1 | 90. | Safety rod | 2 |
| 38. | O-ring d18×2.65 | 1 | 91. | Nut M10 | 2 |
| 39. | Pump plunger | 1 | 92. | External scissors lever | 1 |
| 40. | Y-ring | 1 | 93. | Bushing | 2 |
| 41. | Pump body for plunger | 1 | 94. | Roller for chassis | 2 |
| 42. | O-ring D28×3.1 | 1 | 95. | Internal scissors lever | 1 |
| 43. | Pump body | 1 | 96. | Pin axle for chassis | 1 |
| 44. | O-ring d10.6×2.65 | 1 | 97. | Spring washer 8 | 1 |
| 45. | Spring | 1 | 98. | Hex screw M8×16 | 1 |
| 46. | Reflux rod | 1 | 99. | Pin axle for scissons | 1 |
| 47. | O-ring d4×1.8 | 1 | 100. | Pin axle for table | 1 |
| 48. | Guide casing | 1 | 101. | Bushing | 2 |
| 49. | Protect casing | 1 | 102. | Bolt M8×12 | 1 |
| 50. | Lever | 1 | 103. | Oil cup | 2 |
| 51. | Lever bushing | 1 | 104. | Bolt M6×8 | 1 |
| 52. | Washer 6 | 2 | 105. | Screw M6×30 | 1 |
| 53. | Spring washer 6 | 2 | 106 | Cover-type nut M6 | 1 |
| A | Pump ass’y | 1～49 |
| B | Swivel wheel ass’y | 72 |
| C | Front wheel ass’y | 77 |
| D | Sealkit ass’y | 1,3,4,7,8,9,16,23,25,31,35,37,38,40,42,44,47 |
| E | Handle ass’y | 52,53,55,57,58,59,63,64,105,106 |