Module Nitrogen Generator

- User Manual -

GSE Tech (Suzhou) Co., Ltd

Building 8, No. 98 Hengshan Road, SND,Suzhou. China

POST :215009                FAX :0512-68086515

TEL: 	SALES                 +86-512-65111668

SERVICES           +86-512-66385515

WEB SITE ：http://www.gsetech.cn

CATALOG

１．Technical Parameters

1.1 Design Parameters

1.2 Capability Parameters

1.3 Utilities

２. Safety

2.1 Application

| 2.2 | Preventing Accident |
| --- | --- |
| 2.3 | Danger Source |

３. Function and System Structure

| 3.1 | Using CMS to separate air |
| --- | --- |
| 3.2 | Pressure Swing Adsorption |
| 3.3 | Process flow |

3.4 Air compressor and purification system

3.5 Air Separation

3.6 Nitrogen Storage and Supply

４. Installation

4.1 Installation Requirement

4.2 Normal Installation way

５. Operation

| 5.1 | Control System |
| --- | --- |
| 5.2 | Control process |
| 5.3 | Oxygen Detector |
| 5.4 | Start-up |
| 5.5 | Shut-down |
| 6. Maintenance and Troubleshooting |  |
| 6.1 | Daily Check and Maintenance |
| 6.2 | Possible Malfunctions and Troubleshooting |  |
| 6.3 List of spare parts |  |
| 7. Appendix |  |  |
| 7.1 | Flow Diagram |  |
| 7.2 | Electrical Diagram |  |  |

TECHNICAL PARAMETERS

1. Technical Parameters

1.1 Design Parameters

Requirement of Compressed Air	：

Compressed Air Flow:			                 ≥2225CFH（63Nm3/h）

Compressed Air Pressure :	               ≥101.5PSI（0.7MPa）

Compressed Air Dew Point:				   35.6~50℉（2℃-10℃）

1.2 Capability Parameters

The Request of Nitrogen ：

| N2 Flow |  | 370.8CFH(10.5 Nm3/h) |
| --- | --- | --- |
| Purity |  | ≥99.99%（anaerobic） |
| O2 content |  | ≤0.01% |
| N2 Dew Point |  | ≤-104℉ (≤-40℃）（atmospheric pressure） |
| N2 Pressure |  | 87PSI（0.6MPa） |
| 1.3 Utilities |  |
| Power Voltage： | 115V/1ph/60Hz |
| Power： |  | 0.47hp(0.35kW) |

SAFETY

2. Safety

It is necessary to thoroughly read this manual first before using the equipment, and operate and maintain it strictly according to instructions so as to avoid causing of equipment breakdown. GSE Tech (Suzhou) Co., Ltd. will be responsible for the guarantee of the equipment. However, GSE Tech(Suzhou)Co.,Ltd. will not take the responsibilities for damages caused by user’s improper operation or faults.

2.1 Application

PSA nitrogen generator system is designed with flow and purity described in chapter 1.2. However, without the permission of GSE Tech (Suzhou) Co., Ltd. may not be changed as follows：

·Setup changing goes beyond the limitation stated in part 1.2 ·Changing Hardware setup in system

If the above situations happen, the quality-guarantee is invalid.

2.2 Preventing Accident

All standards of preventing accidents are prescribed by Legal department of country.

Operator should be complying rigorously.

3.3 Danger Source

Healthy Harm！

SAFETY

Compressor, dryer and PSA System may run automatically under the mode of automatic manipulation. Therefore, before maintenance, the whole system and all parts of system must be shut down.

Fire！

Waste gas generated by the system contains nearly 35% highly concentrated oxygen, it is easy to cause fire. Thus this machine should be placed outdoors or the place with good ventilation, and smoking is strongly prohibited.

Asphyxia!

Nitrogen which generated by the machine will not provide enough oxygen for breathing.

Thus product gas should not be used to breath.

Healthy Danger！

All parts of the equipment and pipelines are in high pressure and gas will expand immediately when disassembling and cause directly or indirectly damage to humans. So, high pressure gas in all vessels and pipelines should be released before maintenance.

FUNCTION AND SYSTEM STRUCTURE

3. Function and System Structure

Nitrogen will be generated by separating Oxygen from air through Pressure Swing Adsorption technology.

3.1 Using CMS to separate air

CMS (Activated Carbon Molecular Sieve) is a specially treated material. It is used to separate air.

drawing 3.1	Separating Air（CMS）

The diameter of the holes in CMS is between the diameter of nitrogen molecule and oxygen molecule. It is because of oxygen molecule’s bulk is smaller and lighter than nitrogen molecule that oxygen is Adsorbed prior to nitrogen. See drawing 3.1.

3.2 Pressure Swing Adsorption

More and more molecules will be adsorbed in the surface of CMS, see drawing 3.2.

FUNCTION AND SYSTEM STRUCTURE

Compressed air goes into one adsorption tank and flows from the bottom to the top of the tank.

drawing 3.2	Pressure Swing Adsorption（PSA）

The adsorption tower is filled with molecular sieves and when the gas goes through from the bottom to the top, the oxygen molecule and nitrogen are both adsorbed on the surface of the molecular sieves. However, the quality of oxygen is more than nitrogen molecules. In that way the nitrogen gas goes from the outlet from the tower while most oxygen is adsorbed.

The adsorption time depends on the airflow rate. The relation is explained as following:The higher air flow rate and shorter adsorption time will result in higher nitrogen concentration.

FUNCTION AND SYSTEM STRUCTURE

★ The lower air flow rate and longer adsorption time will result in lower nitrogen concentration.

When adsorption of adsorbent reaches to saturation, it needs regeneration. The

regeneration is caused by decompression. Due to the features of gas adsorption, it provides de-adsorption under low pressure. Therefore the adsorption and regeneration of adsorbent can be repeated according to the principle stated above, assuring the continuous production. When one absorber is regenerating, the other absorber is in working.

3.3 Process flow

PSA Nitrogen Generator Process can be divided into three units:

· Air compressor and purification system

· Oxygen and nitrogen separation unit

· Nitrogen storage and supply

3.4 Air compressor and purification system

The compressed air (about 116PSI (0.8 MPa) ) first enter into the 9 grade filter to remove most water, other condensed liquid which is larger than 3μm (remnant oil less than 5ppm w/w). Then the refrigeration dryer will take most oil, water and dust from compressed air. The latter 7 grade filter will further remove the liquid water, oil and solid granule which is larger than 1μm (Remnant oil less than 1ppm w/w).

Next step, the 3 grade filter will remove solid granule larger than

0.01ppm w/w). Finally, the 1 grade filter will absorb oil vapor and hydrocarbon vapor to 0.003ppm

FUNCTION AND SYSTEM STRUCTURE

0.01μm(Remnant oil less than w/w, which meets the demand of PSA system.

Under rated running conditions, the 1 grade filter can normally work continuously for more than 4000 hours.

After activate carbon tank, the compressed air will reach the required specifications:

  - Oil remaining amount in the air: ≦0.003mg/m3 (70℉(21℃))

  - Solid particulates dimension: ≦0.01μm

  - Moisture remaining amount in the air: ≦5.57g/m3

The condensed water from compressed air will discharged to specific place through pipeline.

3.5 Air Separation

After air purification system, compressed air enters into Adsorber A or B for adsorption through pneumatic valve PV102 or PV103.

Adsorption column A or B with carbon molecular sieve, is the main part of the nitrogen generator, the oxygen and nitrogen separation is done here.Carbon molecular sieve compressing adopt automatic pressing device .

The whole process flow is controlled by 8 valves from PV101 to PV108. See the Table 3-1.

FUNCTION AND SYSTEM STRUCTURE

3-1 Periodic Procedures

| Status |  | Valve Opening | Description |
| --- | --- | --- | --- |
| Adsorption in A | and | PV101、PV102、PV106、 | Adsorption and separation in A and |
| regeneration in B |  | PV108、PV105 | regeneration in B |
| Pressure balance in A and | PV102、PV103、 | Pressure balance of these two towers, |
| B |  | PV106、PV107 | adsorption and preparation for regeneration |
| Regeneration in A | and | PV101、PV103、PV107、 | Regeneration in A and adsorption and |
| adsorption in B |  | PV108、PV104 | separation in B |
| Pressure balance in A and | PV102、PV103 | Pressure balance of these two towers, |
| B |  | PV106、PV107 | adsorption and preparation for regeneration |

3.6 Nitrogen Storage and Supply

· Nitrogen storage tank :

Material: carbon steel, easy to clean, pipe material selection of stainless steel, the welding is reliable.

In accordance with, "container safety supervision regulation of pressure vessel" implementation design, a nitrogen tank and pipeline design pressure is greater than or equal to 145PSI (1.0MPa).

Buffer, by PSA process caused by pressure fluctuation that adsorption tower A and B in adsorption at the start of the pressure minimum.

Ensuring the adsorption tower, A and B in adsorption at the start of the minimum pressure value, its role is buffered by PSA process caused by pressure fluctuation.

The nitrogen flow is adjusted by manual valve V107 through flow meter F101 and then enters application point. The flow meter F101 shows the real flow that output.

The device configuration on gas flow meter, product function, unit L/min.In general, the flow-meter calibration under normal conditions, specific conversion as follows:

The sampling pipe was installed in nitrogen outlet to detect the nitrogen purity.

INSTALLATION

4.1 Installation Requirement

1）Clean and dry compressed air

- 120V/60Hz power

4.2 Normal installation way

The nitrogen generator should be laid on the tidy and horizontal ground. A place with good ventilation is needed. If it is placed in a sealed area, air with over-oxygen and unqualified nitrogen should be emitted outdoors with pipes.

OPERATION

5．Operation

5.1 Control system

SIEMENS CPUSR30 Type PLC is applied to this control system. 8 pneumatic valves will be controlled by the PLC. Oxygen analyzer detects oxygen concentration and when the concentration exceeds the setting value, the PLC will alarm to call attention to the manipulators to open the unqualified gas outlet valve and close the nitrogen outlet valve to prevent unqualified nitrogen going to the next system.

5.2 Process Control

·Main Process Control :

The system is composed of PLC and pneumatic valves PV101- PV108. Pneumatic valves open and close as programmed to accomplish adsorption, regeneration and pressure balance of the PSA system.

·Instruction to Control Panel :

Control cabinet operation panel on the  touch screen display, pressure gauge,. See drawing 5-1.

OPERATION

Drawing 5-1 Control panel display

1. HMI （A1）

Display all the valve working condition as well as the adsorption time.

Press“Start”--N2 Generator start to work.

Press“Stop”--N2 Generator stop work.

Press“Setup”--Parameter setting.

Oxygen Content: ppm of oxygen content in N2

N2 Flow Rate: Flow rate of N2 out

State of Generator: Green,PLC work,N2 Generator work;Red ,PLC stop work,N2 Generator stop work;

Setup  LOGON  :   admin   password:68213687

2.Pressure gauge(P1、P2、P3、P4):

P1-P4 show the Pressure of Air Inlet;adsorber tower A;adsorber tower B and nitrogen tank

5.3 Oxygen analyzer

The remnant oxygen content is detected by the oxygen analyzer continuously

The sampling pipe is composed by:

·The relief valve to adjust the sampling gas pressure ·The regulating valve to adjust the sampling gas flow

Detect the remnant oxygen content ：

- Adjust the sampling pressure to 14PSI (0.1MPa)

- Adjust the sampling flow till the gas can be felt

- The oxygen content can be obtained when the reading is stable

To keep the oxygen analyzer in precision, Calibration is needed regularly. At the meantime, the sampling flow and pressure should be checked in a fixed time. See the instruction of the oxygen analyzer.

Caution:There are three  minutes for oxygen analyzer preheat from the Power ON. During this period, it is forbidden to start the nitrogen generator,otherwise the valve will act abnormally.

5.4  Start-Up:

- Start the air compressor and make it meet the requirements of this machine (required conditions). Open the inlet valve of nitrogen equipment and adjust the pneumatic valves gas source valve to 73~87PSI (0.5-0.6MPa).

OPERATION

- Turn on the switch of nitrogen generator and oxygen analyzer on the control panel. Then set the allowed max value on the oxygen analyzer. Whether they two adsorption towers work normally are judged by the pressure switch between the two towers. During normal working, the pressure of the adsorption tower should be almost the same as the compressed air (perhaps lea than 7PSI (0.05MPa) ) while the regeneration pressure is 0. At the balance stage, the two towers has the same pressure (about a half of the adsorption pressure).

- Turn on the oxygen analyzer and open the sampling valve to regulate the pressure to 14.5PSI( 0.1MPa). And then adjust the sampling flow till the gas can be felt by hands. Notice the sampling flow should not too large.

- The purity and flow rate of nitrogen can be adjusted by adjusting the opening of nitrogen outlet valve V107.

5.5	Shut Down:

- Press “STOP”

- close nitrogen product outlet valve and sampling valve.

(C) Inlet valve of compressed air shall be closed.

(D) Switch of nitrogen machine shall be turned off.

POSSIBLE MALFUNCTIONS AND TROUBLESHOOTING

6.1 Daily Maintenance and inspection

| Inspection | Inspection method | Rated value | Period |
| --- | --- | --- | --- |
| Filter |  |  |  |
| Discharge | Check whether there is effluent |  | Daily |
|  | from the discharge outlet |  |  |
| Clean of the |  |  |  |
| build-in | Take the valve apart and clean in |  | Every |
| discharge valve | neutral solution |  | week |
| The compressed air buffer tank |  |  |
| Pressure gauge | Check whether the pressure is in |  | Daily |
|  | normal range |  |  |
| Discharge valve | Check whether there is effluent |  | Every two |
|  | from the discharge outlet |  | hours |

PSA System PSA

| Oxygen | Check the sampling flow and | The gas can be felt |  |
| --- | --- | --- | --- |
|  | pressure, if needed, adjust them. | by hands | Daily |
| analyzer |  |  |  |
|  | Check the flow meter and adjust it if |  |  |
| Flow meter | needed. The flow should not be |  | Daily |
|  | larger than the rated flow |  |  |
| Pressure gauge | Check whether they work normally |  | Daily |
| Nitrogen | Make sure there is no leakage |  | Every three |
| pipeline |  |  | months |

Note: See the instruction of the compressor and dryer to get the maintenance method.

CAUTION: The nitrogen generator must be shut down when the compressor or dryer has fault.

POSSIBLE MALFUNCTIONS AND TROUBLESHOOTING

6.2 Possible Malfunctions and Troubleshooting

| Appearance | Possible reasons | Treatment |
| --- | --- | --- |
|  | Nitrogen flow | too | Check the nitrogen flow |
| Analyzer alarm | high |  |  |  |
| O2 |  |  |
|  | Set value not correct | Check the set value |
| Pneumatic valve can not open | PLC problem | Check whether the PLC output light is on, if not, |
|  |  | the PLC should be changed to a new one |
|  | Gas source pressure too low | Make sure the gas source pressure larger than |
|  |  | 4bar, or check whether there is any leakage |
|  | The valve rod get stuck | If there is no the above appearance, take the copper pipe joint apart from valve and check weather there is gas from copper pipe. If yes, take the head apart from the valve and force the rod move up and down several times. |

|  | The solenoid valve coil is burnt | If there is no the above appearance, Check the corresponding solenoid valves and check whether the wiring is fixed or not. If the coil is burnt, change the solenoid valve. |
| --- | --- | --- |
| There is a lot of black dust from Muffler or flow meter | The activate carbon or molecular sieves is disclosed | Contact us |
| Nitrogen flow is not enough while the Pressure is normal | The terminal filter or check valve is stuck | Take them apart and clean, change a new one when they are not maintainable |

6.3 List of  spare parts

| S.N. | Name | Number | PCS | Replacement cycle | Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Air Filter element | 180238 | 1 | Half a year | F104 |
| 2 | N2 Filter element | 180213 | 1 | a year | F105 |
| 3 | Silencer | 180004 | 2 | a year | SL101/102 |
| 4 | Pressure reducing filter | 180679 | 1 | 2 years | V103 |
| 5 | Solenoid valve | 181421 | 8 | 5 years |  |
| 6 | 2-way Pneumatic valve | 180002 | 8 | 5 years | PV101-PV108 |
| 7 | Oxygen analyzer | 180540 | 1 | 5 years | AIA O2 |
| 8 | CMS | 180648 | N | 8 years |  |

APPENDIX

7. Appendix

| 7.1 | Flow Diagram |
| --- | --- |
| 7.2 | Electrical Diagram |  |