## Instruction Manual

# Fork Extensions

Note: The Owner/Operator must read carefully and understand

all the information presented here before operation.

Thank you for choosing our FORK EXTENSIONS. For your safety and correct operation, please carefully read the manual before use.

NOTE: All of the information reported herein is based on data available at the time of printing. The factory reserves the right to modify its own products at any time without notice or incurring in any sanction. Please verify with the factory for possible updates.

EX series is a tool for forklift, and it is an extension of the fork. You can choose the relevant fork extension according the length of object. It is used to lift or transport the longer or bigger object.

1. SPECIFICATION

| Model | Length of Extension | Fit Fork Width | Net Weight (per pair) |
| --- | --- | --- | --- |
|  | Inch | mm | Inch | mm | lbs | kg |
| EX484 | 48 | 1219 | 4 | 100 | 77.5 | 35 |
| EX604 | 60 | 1525 | 4 | 100 | 97 | 44 |
| EX724 | 72 | 1830 | 4 | 100 | 116 | 53 |
| EX844 | 84 | 2134 | 4 | 100 | 136 | 62 |
| EX964 | 96 | 2435 | 4 | 100 | 155 | 70 |
| EX485 | 48 | 1219 | 5 | 125 | 87 | 39 |
| EX605 | 60 | 1525 | 5 | 125 | 108 | 49 |
| EX725 | 72 | 1830 | 5 | 125 | 130 | 59 |
| EX845 | 84 | 2134 | 5 | 125 | 152 | 69 |
| EX965 | 96 | 2435 | 5 | 125 | 173 | 79 |
| EX486 | 48 | 1219 | 6 | 150 | 94 | 43 |
| EX606 | 60 | 1525 | 6 | 150 | 117.5 | 53 |
| EX726 | 72 | 1830 | 6 | 150 | 141 | 64 |
| EX846 | 84 | 2134 | 6 | 150 | 164.5 | 75 |
| EX966 | 96 | 2435 | 6 | 150 | 188 | 85 |

2. PACKING

This product is packed with the carton or steel packing. When open the packing, please check carefully whether it is good or has other problem. If it is damaged, please fill in the list to mail provider and recode the model you bought.

3. Cautions

WARNING: Please pay attention to the operation as follows for using correctly.

- Product center “P”shouldn’t exceed the center of lengthen of lengthen fork.

- The load of the center of lengthen fork,”P”,is counted by the formula below.

P=T-70×(A-L/2)÷25

T=2500kg

A is the lengt from the center of lengthen fork to the back of fork.(mm);

L is the lenthen of fork..

- You must choose the fork extension matching with the fork; otherwise it will influence the load on the fork or operating safety.

- Do not damage and delete the warning label.

- Please check carefully before using it, and if it

- Do not modify this product without the permission of the manufacture.

4. OPERATING INSTRUCTION

- Please put the fork extension evenly by worker or tool for fitting the socket of the fork extension.

- U-Bolt must be under the fork.

- U-Bolt need to include the root of the fork to avoid the fork extension sliding from the fork.

5. MAINTENANCE

This product is a jointing construction divided tow pieces. Please usually check the fork extension. If there is any distortion, contact the provider in time.

6. LIMITED WARRANTY

The product for 1 year when used properly within its rated capacity. The customer assumes liability for any modifications, unauthorized, repairs or parts substitution.