# Instruction Manual

## HAND PALLET TRUCK（11000lb）

Note: Owner/Operator must read and understand this instruction

manual before using the hand pallet truck.

Thank you for choosing our pallet truck. For your safety and correct operation, please

carefully read the manual before use.

- GENERAL SPECIFICATIONS

| Model | HP50 |
| --- | --- |
| Capacity (lb) | 11000 |
| Max. Fork Height (inch) | 8 |
| Min. Fork Height (inch) | 3.5 |
| Fork Length (inch) | 45.3 |
| Width Overall Forks (inch) | 22.8 |
| Individual Fork Width (inch) | 8.3 |
| Load Wheel Diameter (inch) | Ø3.1 |
| Steering Wheel Diameter (inch) | Ø7.9 |
| Net Weight (lb) | 433 |

- TO ATTACH HANDLE TO PUMP UNIT

1. Handle assembly   2. Screw   3.Iron sheet   4.C-type clip

5. Pin   6. Bracket    7. Spring pin   8. Pump unit and Frame

2.1 Take out two pins (5) and two spring pins (7) from the plastic bag wrapping on

the handle assembly (1).

2.2 Undo two screws (2) and iron sheets (3) on C-type clip (4).

2.3 Insert down end of handle assembly (1) into the bracket (6), please note: Feed the rod

and chain (H802) through the center of bracket (6).

2.4 Install the two pins (5) to connect the handle assembly (1) and bracket (6).

2.5 Install the two spring pins (7).

2.6 Press down the handle assembly (1) and take out C-type clip.

2.7 Loosen the setting screw (140H) on the crank link (5010).

2.8 Raise the crank link (5010) and put the pin on rod and chain (H802) into the groove of

crank link (5010).

- TO ADJUST RELEASE DEVICE

On the handle of the pallet truck, you will find the control lever (H106) which can be set

in three positions (See Fig. 1):

LOWER=to lower the forks; NEUTRAL=to move the load; ASCENT=to raise the forks.

After assembling the handle, you can adjust the three positions.

3.1 First tighten the setting screw (140H) on the crank link (5010) until the LOWER position function works.

3.2 If the forks elevate while pumping in the NEUTRAL position, turn the setting screw (140H) clockwise until pumping the handle does not raise the forks and the NEUTRAL position functions correctly.

3.3 If the forks descend while pumping in the NEUTRAL position, turn the setting screw (140H) counter-clockwise until the forks do not lower.

3.4 If the forks do not descend when the control lever (H106) is in the LOWER position, turn the setting screw (140H) clockwise until raising the control lever(H106) lowers the forks. Then check the NEUTRAL position as per item 3.2 and 3.3.

3.5 If the forks do not lift while pumping in the ASCENT position, turn the setting screw (140H) counter-clockwise until the forks elevate while pumping in the ASCENT position.  Then check the NEUTRAL and LOWER position as per item 3.2, 3.3 and 3.4.

- MAINTENANCE

4.1 OIL

Please check the oil level every six months. The oil capacity is about 0.3lt. Restore the fluid

level in the rubber reservoir to 5mm below the top, this must be with the forks in the lowered

position.

Add or change the hydraulic oil according to the table below.

| Temperature | Oil |
| --- | --- |
| -20℃~+40℃ | L-HV46 Hydraulic oil |

4.2 HOW TO EXPEL AIR FROM THE PUMP UNIT

Air may enter the unit when the seals are replaced. Lift the control lever (H106) to the

LOWER position, then move the handle up and down for several times.

4.3 DAILY CHECK AND MAINTENANCE

Daily check of the pallet truck can limit wear and tear of the unit. Pay special attention to the

wheels (5031, F5008), the axles (F5006, F5009, F5011, F5014), the handle (H801), the forks (F5002) and lift and lower control. When the truck is not being used, it should be left in the lowered position.

4.4 LUBRICATION

Use motor oil or grease to lubricate all moveable parts.

- SAFETY RULES AND OPERATING INSTRUCTIONS

For safe operation of the Hand Pallet Truck, please read all warning signs and instructions here and on the pallet truck prior to use.

  - Safety rules

To avoid hazardous situations, you should obey the following rules:

- Fall Hazard

Do not use as a personnel lifting platform or step.

- Tip-over Hazards

Do not overload the machine.

The machine can be only used on a firm, level surface.

Do not use the machine on the condition of drop-offs, holes, bumps, debris, unstable surfaces or other possible hazardous conditions.

The machine can be only used in the light environment of at least 50LUX.

- Collision hazards

Do not lift if the load is not properly centered on the forks. Check the “Diagram of correct centered load” on the manual for correct load center position.

Check the work area for overhead obstruction or other possible hazards.

4)  Bodily Injury Hazards

Recommended operators to wear safety shoes and gloves.

Do not put the hands and feet under the forks when using the machine.

5)  Improper Use Hazard

Never leave a machine unattended with a load.

- Damaged Machine Hazards

Do not use a damaged or malfunctioning machine.

Conduct a thorough pre-operation inspection prior to each use.

Be sure that all decals are in place and legible.

- Lifting Hazard

Use proper lifting techniques to load the machine.

5.2 Operating instructions

─── Do not operate the machine unless you have been trained and authorized.

─── Check the machine prior to use, pay special attention to the wheels, the hand assembly, the forks and lift and lower control.

─── The machine shall not be used on gradients, if it is necessary to negotiate slopes, the gradient shall be no more than 2%, and the machine shall be unloaded, the forks shall be facing downgrade.

─── Never place any part of your body in the lifting mechanism or under the forks on load.

─── Do not carry passengers.

─── We advise that operators should wear gloves and safety shoes.

─── Do not handle unstable or loosely stacked loads.

─── Do not overload the machine.

─── The handle shall not be turned right to stop.

─── The machine shall not be used as a vehicle jack.

─── The extremity of fork arms shall not be used as a lever to lift a load.

─── The machine shall not have direct contact with foodstuffs.

─── The machine shall not be used in a potentially explosive atmosphere.

─── When the machine is using in the truck, it can not be loaded extremely heavy goods, so as to bumping the operators or losing the control of the machine.

─── The machine shall not be used unbalanced load.

─── The machine shall not be used undesignedly moving hazard situations.

─── When the machine is loading:

- Push the machine, the height of the load can not exceed the sight of the operators;

- The machine shall be moved slowly and smoothly, so as to occur the bump hazard;

- While moving no part of the fork arms or of the load shall come into contact with an obstacle;

- During lowering the load neither the fork arms nor the load shall rest upon an obstacle.

─── Lower the forks to lowest height without load when the machine is not being used.

- TROUBLES SHOOTING

| NO | TROUBLE | CAUSE | ACTION |
| --- | --- | --- | --- |
| 1 | The forks do not lift to maximum height. | -Not enough hydraulic oil. | -Add more oil. |
| 2 | The forks do not lift up. | -Not enough hydraulic oil. -The oil has impurities. -Discharge valve is out of adjustment. -Air in the hydraulic oil. | -Pour in more filtered oil. -Change the oil. -Adjust the setting screw (140H). -Expel the air. |
| 3 | The forks do not descend. | -The rod (5002) and the cylinder (5022) are deformed resulting from a seriously unbalanced load. -A part has been broken or been deformed resulting from unbalanced load. -The setting screw (140H) is not in the correct position. | -Replace the rod (5002) or cylinder (5022). -Repair or replace component. -Adjust the setting screw (140H). |
| 4 | Leaks | -Seals worn out or damaged. -Some parts may be cracked or worn out. | -Replace seals with new ones. -Check and replace with new ones. |
| 5 | The forks descend without being lowered. | -Impurities in the oil cause the discharge valve (B) to fail to close. -Air in the oil. -Seals worn or damaged. -Discharge valve (B) is out of adjustment. | -Replace with filtered oil. -Expel the air. -Replace with new ones. -Adjust the setting screw (140H). |

*NOTE: DO NOT ATTEMPT TO REPAIR THE PALLET TRUCK UNLESS YOU ARE TRAINED AND AUTHORIZED TO DO SO.

Attached list of repair and maintenance record (Attached list A)

- TRANSPORTATION AND STORAGE OF THE MACHINE

─── The machine is packed in wood pallet, six in one wood pallet, each machine is packed with corrugated paper, and each weight is 197kg.

─── Pay attention to the balance while hanging and unloading, do not bump, so as to occur fall hazard.

─── Pay attention while disassembling the package, person or machine shall not be scraped by the sheet iron of the pack.

─── The machine shall be stored in dry room.

5

Parts  List  of  Pump  Assembly

| PARTS NO. | DESCRIPTION | Q’ty | PARTS NO. | DESCRIPTION | Q’ty |
| --- | --- | --- | --- | --- | --- |
| 5001 5002 5003 5004 5005 5006 5007 5008 5009 5010 5011 5012 5013 5014 5015 5016 5017 5018 5019 5020 5021 5022 5023 5024 5025 5026 5027 5028 5029 5030 | Steel ball Rod Dust proof ring O-ring Cylinder O-ring Washer Seal ring Spring pin Crank link Pump rod Spring washer Spring cover Big spring Dust proof ring O-ring Pump cylinder Seal ring Nylon bushing Red copper washer Spring pin Cylinder Bushing Bearing Spring pin Rhombus plate Dowel pin Retaining ring Retaining ring Bearing | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 2 1 2 1 2 4 | 5031 5032 5033 5034 5035 110 111 112 113 114 115 116 117 118 119 129 130 131 132 133 134 135 136 137 138 140H 141 166 167 | Iron wheel Steering wheel axle Spring pin Pin O-ring Screw Red copper washer Spring Pressure rod Steel ball Pressure valve body Split ring O-ring Red copper washer Steel needle Steel ball Discharge valve body Spring O-ring Discharge valve shaft Valve taper core Spring Pressure regulating screw O-ring Screw Setting screw Nut Retainer Retainer | 2 1 2 2 1 1 1 1 1 1 1 1 2 2 1 1 1 1 1 1 1 1 1 2 2 1 1 3 1 |

## Parts   List   of   Frame

| PARTS NO. | DESCRIPTION | Q’TY | PARTS NO. | DESCRIPTION | Q’TY |
| --- | --- | --- | --- | --- | --- |
| F5001 F5002 F5003 F5004 F5005 F5006 F5007 F5008 F5009 F5010 F5011 | Spring pin Frame Torsion tube shaft Spring pin H-link Load roller axle Bearing Load roller H-link axle Parallel pin Roller axle | 1 1 1 6 2 4 8 4 2 2 2 | F5012 F5013 F5014 F5015 F5016 F5017 F5018 F5019 F5020 F5021 | Wheel frame Roller Axle Rod Pin Fork joint Retaining ring Torsion tube assembly Bushing Hex socket screw | 2 2 2 2 2 2 2 1 4 1 |

# Parts  List  of  Handle

| PARTS NO. | DESCRIPTION | Q’ty | PARTS NO. | DESCRIPTION | Q’ty |
| --- | --- | --- | --- | --- | --- |
| H801 H802 H803 H804 H805 H806 H102 | Handle Rod and chain Setting screw Shaft Steel roller Bushing Spring pin | 1 1 1 1 1 2 1 | H103 H104 H105 H106 H108 H111 H112 | Spring leaf Spring pin Spring pin Control lever Rubber cushion Nylon roller Spring pin | 1 2 1 1 1 1 1 |