INSTRUCTUCTION MANUAL

ICDH

Note: Owner/Operator must read and understand this instruction manual before using the clamp.

General

This manual contains important information for the correct installation, operation, and maintenance of the equipment described herein. The use of any clamp presents some risk of personal injury or property damage. All persons involved in such installation, operation and maintenance should be thoroughly familiar with the contents of this manual. To safeguard against the possibility of property damage or personal injury follow the recommendations and instructions of this manual and keep it for further reference.

Aside from transporting plate, this clamp is well-suited to turning over steel structures and welded constructions.

All plate clamps have been manufactured in accordance with the Machinery Directive 98/37/EC.

They are type-tested 4 to 1 against breakage. Each unit is proof-tested 1.5 times of the rated load.

Do not use the clamps in areas containing flammable vapors, liquids, gasses or combustible dust or fibers. Do not use the clamp in highly corrosive, abrasive, wet environments or in applications involving exposure to temperatures below -40°C or above 80°C

Specification

| Dimensions |
| --- |
| Model | A | B | C | D | E | F | G | H | I | J |
| 1t | 24 | 33 | 125 | 50 | 24 | 220-260 | 30 | 156 | 54 | 14 |
| 2t | 39 | 45 | 155 | 55 | 30 | 250-295 | 36 | 175 | 60 | 16 |
| 3t | 46 | 49 | 182 | 50 | 36 | 296-360 | 40 | 220 | 72 | 18 |
| 5t | 55 | 55 | 222 | 60 | 45 | 350-420 | 60 | 270 | 76 | 18 |
| 8t | 70 | 60 | 240 | 65 | 40 | 450-510 | 66 | 275 | 90 | 22 |
| 10t | 95 | 75 | 285 | 80 | 45 | 470-590 | 70 | 330 | 95 | 25 |
| 12t | 100 | 125 | 360 | 80 | 30 | 500-600 | 90 | 360 | 110 | 25 |

| Performance Parameter |
| --- |
| Model | Lifting capacity(kg) | Test load(kg) | Jaw opening(kg) | Net weight(kg) |
| 1t | 1000 | 2000 | 0-22 | 3.6 |
| 2t | 2000 | 4000 | 0-30 | 5.5 |
| 3t | 3000 | 6000 | 0-40 | 10 |
| 5t | 5000 | 10000 | 0-50 | 17 |
| 8t | 8000 | 16000 | 0-60 | 26 |
| 10t | 10000 | 20000 | 0-80 | 32 |
| 12t | 12000 | 24000 | 0-90 | 48 |

Installation

3.1 Estimate the plate that is to be lifted or moved and make sure it does not exceed the rated load of the clamp.

3.2 This clamp with pivoting shackle can be used for lifting and transporting plate at various angles, but the load capacity is reduced, as seen on the diagram below showing the load/force capacities.

3.3 The pivoting shackle has the added advantage of providing enough clamping force to hold a plate safely, even when transport large-sized plates with the 2-legged lifting system. Slipping or damage to the clamp is prevented.

When using two clamps to transport large-sized plates, pay attention to the reduced capacities of the clamps.

The inclination angles are from 40˚ to 60˚ as picture. Inclination angles larger than 60˚ are not allowed.

3.4 Make sure that the plate surface must have a hardness below HRC 30/ HB 300.

3.5 Make sure that the support to which the pivoting shackled is attached is strong enough to hold several times the weight of the plate.

4. Operation

Warning

To avoid damage and/or personal injury:

1 .Do not exceed maximum load of the clamp.

2. Do not use the clamp to lift or transport people.

3. Do not use damaged clamp or clamp that is not working properly.

4. Do not lift or transport loads over people and make sure all personnel remain clear of supported plate.

5. Do not lift the plate that is not fully engaged with the clamping jaws.

6. Do not leave load supported by the clamp unattended unless specific precaution have been taken.

7. Do not lift loads that are not balanced, and the holding action is not secure.

SAFETY WARNING

Never Exceed Maximum Capacity

These clamp models feature a specially developed “hard’’ segment and “hard’’ pin so that these lifting clamps can be used for lifting steel sheets and/or structures with a maximum hardness of 30 HRC, (300 HB).

4.1 Attaching the plate

Turn the function lever clockwise to disengage the jaws. Then put the plate to the end of the mouth of clamp. Move the function lever counter- clockwise to grip and lock the plate.

4.2 Danger zones

Do not lift or transport loads while personnel are in the danger zone.

Do not stand or place hands or feet under the raised plate.

Raised loads are not to be left unattended for a longer period of time.

The operator may only start to move the load when he is sure the load will not overturn and that all personnel have left the danger zone.

4.3 To unload

Pull the function lever to disengage the jaws.

5. Maintenance/Inspection

Check the general condition of the clamp at least once a month.

- Stop using the clamp if:

- The body is split or deformed, in particular in way of the corners of the jaws,

- The lifting shackle and/or connecting piece or MP fork (if applicable) are visibly deformed,

- The cam and/or pivot teeth are no longer sharp,

- The spring has become stretched or broken,

- The lever locking mechanism has become inefficient or has ceased to work,

- The shackle pins are visibly deformed,

- Any retaining pins are missing,

- The keyway groove is dirty,

- The marking on the clamp is no longer legible.

Depending on the defects/malfunctions noted:

- disassemble and clean the clamp or have the clamp overhauled by specialized persons.

6. Parts List

| Item | Description | Quantity | Item | Description | Quantity |
| --- | --- | --- | --- | --- | --- |
| 1 | Pulling ring | 1 | 11 | Washer | 2 |
| 2 | Spring | 1 | 12 | Spring pin | 1 |
| 3 | Spring pin | 1 | 13 | Link shoulder | 2 |
| 4 | Nut | 2 | 14 | Shaft | 1 |
| 5 | Bolt | 1 | 15 | Plate assembly | 1 |
| 6 | Safety latch | 1 | 16 | Jaw holder | 1 |
| 7 | Link pin | 1 | 17 | Lifting ring | 1 |
| 8 | Jaw shaft | 1 | 18 | Bolt | 1 |
| 9 | Bolt | 1 | 19 | Nut | 1 |
| 10 | Jaw | 1 |  |  |  |