Operational Manual

# Fork Type Stacker

Model：PF2085  PF2120  PF4085  PF4120  PF4150

## PJ2085  PJ2120  PJ4085  PJ4120  PJ4150

PJ4170

Note: Please do read carefully and understand completely this

manual before the owner/operator uses the machine.

### Contents

- External Shape & Parameter Form

- Names of the Parts

- Assembly and Debug

- Attention and Warning

- Operational Instructions

- Daily Maintenance and Regular Inspection

- Hydraulic Principle Drawing

- Display of the Combination

- List of the Parts

Thank you very much for using this series of forklifts.

This operational manual has a description of the right operational methods to ensure safety and the maintenance methods to extend the use lifetime.  The operator shall read carefully and completely understand it before using the forklift.

This series of forklifts are mainly used to load, lift and pile goods or take down goods from a certain height on the flat and solid floor.  It is widely used in various plants, markets and warehouses.

This series of forklifts with low forks are especially suitable to transport pallets. Plates attached have the function of platform lift.

- External Shape & Parameter Form

- External shapes of PFA series of forklifts

- Technical parameters of PFA series of forklifts

| P M | H | H1 | H2 | L | L1 | W1 | W | B | d | D | h | Work No. | Load | NW | Platform |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PF2085 | 42.3 | 3.7 | 33.5 | 42.7 | 26 | 4 | 22 | 22 | Ф3 | Ф5 | 1.1 | 18 | 440 | 121 | Lp10(25.8x22.4) |
| PF2120 | 56 | 3.7 | 47 | 42.7 | 26 | 4 | 22 | 22 | Ф3 | Ф5 | 1.1 | 24 | 440 | 136 | LP10(25.8x22.4) |
| PF4085 | 42.3 | 3.7 | 33.5 | 42.7 | 26 | 4 | 22 | 22 | Ф3 | Ф5 | 1.1 | 32 | 880 | 154 | LP20(25.8x22.4) |
| PF4120 | 56 | 3.7 | 47.2 | 42.7 | 26 | 4 | 22 | 22 | Ф3 | Ф5 | 1.1 | 48 | 880 | 167 | LP20(25.8x22.4) |
| PF4150 | 68 | 3.7 | 59 | 42.7 | 22 | 4 | 22 | 22 | Ф3 | Ф5 | 1.1 | 60 | 880 | 180 | LP20(25.8x22.4) |

- External shapes of PJA series of adjustable forklift

- Technical parameters of PJA series of forklifts

| P M | H | H1 | H2 | L | L1 | W1 | W | B | d | D | h | Load | Work No. | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PJ2085 | 42.3 | 3.7 | 33.5 | 42.7 | 26 | 4 | 22 | 22.8 | 3 | 5 | 1.1 | 440 | 18 | 128 |
| PJ2120 | 56 | 3.7 | 47.2 | 42.7 | 26 | 4 | 22 | 22.8 | 3 | 5 | 1.1 | 440 | 24 | 143 |
| PJ4085 | 42.3 | 3.7 | 33.5 | 42.7 | 26 | 4 | 22 | 22.8 | 3 | 5 | 1.1 | 880 | 32 | 165 |
| PJ4120 | 56 | 3.7 | 47.2 | 42.7 | 26 | 4 | 22 | 22.8 | 3 | 5 | 1.1 | 880 | 48 | 178 |
| PJ4150 | 68 | 3.7 | 59 | 42.7 | 26 | 4 | 22 | 22.8 | 3 | 5 | 1.1 | 880 | 60 | 189 |
| PJ4170 | 75.8 | 3.7 | 67 | 42.7 | 26 | 4 | 22 | 22.8 | 3 | 5 | 1.1 | 880 | 72 | 202 |

- Names of the Parts

1) Front Wheel                  2) Chassis Assembly           3) Fork Assembly

4) Work Platform                5) Cylinder Assembly           6) Chains and Wheel

7) Slide way Handrail Assembly    8) Footstep Lever             9) Back Wheel

- Installation and Debug

The parts are packed when delivered out of the factory.  The user can install quickly and easily according to the part numbers in the following order.  Please have two 13, 14 or 17 spanners and other necessary tools beside when fixing.

- Confirm No. 11 is the fork assembly; No. 12, 13 are the handrail and cylinder assembly; No. 14 is the chassis assembly; No. 16 is the connecting bolts (4 sets).  Confirm all these are available.

- On the flat floor, put No. 11 the fork on No. 14 the chassis according to the drawing.

- Make No. 12 handrail go through No. 11 forks and four rolling wheels 15, till the position of No. 14 chassis angle iron.  And also ensure the positioning hole on the bottom of the cylinder pump plate is identical with the positioning bolt of No. 14 chassis cylinder.  Connect tightly and deadly No. 12 the handrail and No. 14 chassis with No. 16 the bolts.

- Connect tightly the bolts of No. 13 cylinder chains and No. 11 fork connecting plates, and use a split safe.

- The forklift height after being installed can be adjusted the parameters specified in this manual by adjusting the chains bolt.

- Make sure all the parts are fixed and the bolts connect tightly and have been adjusted well.

- When operated without load, the forklift rises and falls stably and normally.

- When operated with the rated load, the forklift rises and falls stably, the foot wheels move flexibly and the brake works effectively.

- Attention and Warning

- The forklift shall be used on the flat and hard floor.

2) The load shall not exceed the max. load.  Transport goods strictly according to the load curve to assure the load balance.

- Operational Instructions

- Lock the brake. And close the falling valve pole.

- Operate the rising footstep pole to make the forks rise stably to the max. height. Turn open the falling valve pole, and the forks fall.  Turn and close the falling valve pole so that the forks can stop at any height without sliding down.

- When the load exceeds 1.2 times of the rated load, the safety valve of the cylinder works so that the forks cannot rise and the safety of the operation and equipment are assured.

- When driving the forklift with load, make the forks fall to the lowest position to ensure safety.

- The falling speed of the forks is adjustable by adjusting the angle of the positioning ring on the falling valve pole.

! 6) Don’t operate the rising footstep pole quickly.  Otherwise, the cylinder will run empty.

! 7) The falling valve shall be turned open slowly with heavy load to make the forks fall slowly.  Otherwise, dangers will happen.

! 8)  When the rising operation or stops at any height are done with heavy loads, the falling pole shall be closed tightly.  Otherwise, the forks will fall.

- Daily Maintenance and Regular Inspection

- Daily check if there are any deformations, looseness or abnormal noises of the connecting bolts, wheels, rolling wheels, lifting chains and wheel, the parts of hydraulic cylinder, moving parts.

- Daily check if there is any oil leakage of the hydraulic system.

- Check monthly the wear and tear of the forks, rolling wheels, wheels, chains and wheel.

- After the lifting cylinder runs for 20 hours accumulatively in the beginning, the hydraulic oil shall be changed.  Afterwards the oil shall be changed once every 300 hours.  When the accumulated hours are not so much, change the oil once every 18 months.

Please fill in the specified hydraulic oil at the following

temperatures listed below:

| Temperature | Hydraulic Oil |
| --- | --- |
| -5℃~+45℃ | L-HM68 hydraulic oil (equivalent to ISOVG68) |
| -15℃~ -5℃ | L-HM46 hydraulic oil (equivalent to ISOVG46) |

When changing the oil, adjust the pole of the pillar piston to the lowest position.  The oil shall be filled to the position of the filling hole.

|  | 1 | Out-pushing Cylinder |
| --- | --- | --- |
|  | 2 | Turning Lifting and Falling Valve |
|  | 3 | Safety Valve |
|  | 4 | Oil Returning Valve |
|  | 5 | Work Valve |
|  | 6 | Work Cylinder |

- Hydraulic Principle Drawing

8. Display of the Combination

1) Display of the combination of PF（PJ） series of fixed forklift

9. List of Parts

1) List of the parts of PF(PJ) series of fixed forklift

| PJ(Adjustable Fork）,PF（Fixed Fork）Part Lists |
| --- |
| Item No.# | Part Description | Qty | Item No.# | Part Description | Qty |
| 1 | Handrail Frame Unit | 1 | 40 | Split Cotter Φ3 | 1 |
| 2 | Nut M8 | 2 | 41 | Load Chain Connecting Bolt | 2 |
| 3 | Spring Washer-Φ8 | 2 | 42 | Load Chain Link | 2 |
| 4 | Plain Washer-Φ8 | 2 | 43 | Load Chain 10A | 1 |
| 5 | Cylinder Hoop | 1 | 44 | Socket Plain Cap Screw M6X12 | 2 |
| 6 | Hex.Bolt M10X30 | 4 | 45 | Spring Washer 6 | 2 |
| 7 | Plain Washer Φ10 | 4 | 46 | Plain Washer 6 | 2 |
| 8 | Spring Washer Φ10 | 4 | 47 | Dustproof Cover | 2 |
| 9 | Nut M10 | 9 | 48 | Movable Pulley Mounting base | 1 |
| 10 | Hexagon Cap Nuts M20 | 2 | 49 | Copper bush Φ15X1 | 2 |
| 11 | Spring Washer Φ20 | 2 | 50 | Movable Pulley | 1 |
| 12 | Rear Swivel Castor(5''-M20） | 2 | 51 | Support Shaft | 1 |
| 13 | Platform (for PJ Model Option) | 1 | 52 | Plunger Piston | 1 |
| 14 | Circlip for Shaft Φ12 | 8 | 53 | elastic cylindrical pin Φ5X40 | 1 |
| 15 | Front axle | 2 | 54 | Reset Spring Plate | 1 |
| 16 | Front Wheel Sleeve | 4 | 55 | Reset Spring | 1 |
| 17 | Front Wheel | 2 | 56 | DHS shape Dustproof Hoop 18X26X4.5/6 | 1 |
| 18 | Base Frame,weld Unit | 1 | 57 | UNS shape Seal 18X26X6 | 1 |
| 19 | End Cap Bolt M10x1 | 2 | 58 | Foot Pedal Base Shaft | 1 |
| 20 | Combined Seal Ring Φ10 | 2 | 58a | Pump Ring |  |
| 21 | Steel Ball Φ7 | 3 | 59 | Food Pedal Roller Shaft | 1 |
| 22 | O ring 7.5X1.8 | 2 | 60 | Roller | 1 |
| 23 | elastic cylindrical pin Φ3X18 | 1 | 61 | Foot Pedal Bar | 1 |
| 24 | Release Valve Bar | 1 | 62 | Pedal Cushion Cover | 1 |
| 25 | Cylinder Weld Unit | 1 | 63 | Hexagon socket head screw M6X16 | 4 |
| 26 | Torsional Spring | 1 | 64 | Spacer | 4 |
| 27 | Socket Head Cap Screw M6X16 | 4 | 65 | Support Roller | 4 |
| 28 | Nut M6 | 4 | 66 | Copper bush Φ18X1 | 4 |
| 29 | Fixed Tube | 1 | 67 | Circlip for Shaft Φ10 | 4 |
| 30 | Pressure release lever | 1 | 68 | Copper bushΦ10X1.5 | 4 |
| 31 | Quincunx Knob M10 | 1 | 69 | Side Roler | 2 |
| 32 | End Cap Bolt M8X1 | 1 | 70 | Side Roller Shaft | 2 |
| 33 | Combined Seal Ring Φ8 | 1 | 71 | Circlip for Shaft Φ24 | 2 |
| 34 | "O" Ring 31.5X3.55 | 1 | 72 | Shaft for Adjust Fork | 1 |
| 35 | UNS shape Seal 25X33X6 | 2 | 73 | Fork Weld Unit | 2 |
| 36 | "O" Ring 50X3.1 | 1 | 73a | Platform Weld Unit | 1 |
| 37 | DHS shape Dustproof Hoop 25X33X4.5/6 | 1 | 74 | Fork Base Weld Unit | 1 |
| 38 | Cyclinder Top Cover | 1 | 75 | Big Washer 6 | 1 |
| 39 | Piston Rod | 1 |  |  |  |