INSTRUCTUCTION MANUAL

YC

Note: Owner/Operator must read and understand this instruction manual before using the clamp.

1 .General

This manual contains important information for the correct installation, operation, and maintenance of the equipment described herein. All persons involved in such installation, operation and maintenance should be thoroughly familiar with the contents of this manual. To safeguard against the possibility of property damage or personal injury follow the recommendations and instructions of this manual and keep it for further reference.

Beam clamps are designed to provide a secure semi-permanent suspension or rigging point on a flanged structural beam or joist.

The equipment shown in this manual is intended for industrial use only and should not be used to lift, support, or otherwise transport people.

2. Installation and Operation

Verify that the beam flange width matches clamp flange width specifications. The beam clamp is opened by rotating the threaded bar until the clamp can be positioned on the beam. The clamp is then closed by reversing the rotation of the bar. Make sure that the clamp is being positioned correctly, With the beam flange edges contacting the back of the arm recesses and with the load points testing on top of the flange surface.

Once the clamp is securely attached to the beam, apply the load to the center of he clamp suspension bar, avoiding side pulling. Lift the load a short distance or tension the load to ensure that straight line pull is applied to the clamp, and that beam deflection is not excessive.

3. Threaded Bar Replacement

1. Open clamp as wide as possible.

2. Knock out lock pin in handle.

3. Rotate threaded bar until fully disengaged.

4. Remove old nuts by pushing out through the clamp arms.

5. Remove and clean spacer tubes.

3. Fit new nuts into existing spacer tubes.

7. Fit new threaded bar, entering both nuts simultaneously.

3. Rotate bar until new lock pin can be fitted to handle.

Warning

To avoid damage and/or personal injury:

a. Do not exceed maximum load of the clamp.

b. Do not use the clamp to lift people or loads over people.

c. Do not use clamp on flange widths outside the rated range.

d. Do lubricate the clamp regularly.

e. Do check the clamp prior to use and periodically for cracked, worn or deformed parts.

f. Do check the load capacity of the clamp prior to use.

g. Do follow the instructions for the lifting equipment used with the clamp.

4. Specifications

5. Parts List

| Item | Description | Quantity |
| --- | --- | --- |
| 1 | Body couple with suspension bar | 1 |
| 2 | Wide spacer tube | 1 |
| 3 | Width bar nut (L.H.) | 1 |
| 4 | Threaded bar | 1 |
| 5 | Locking pin | 1 |
| 6 | Handle | 1 |
| 7 | Narrow bar nut (R.H.) | 1 |
| 8 | Narrow spacer tube | 1 |