Horizontal Automatic Band Saw Machine

Model: CS-330HB

Operation Manual

- Thanks for choosing Chenlong Product! We’re honored that you become our client. For purpose of safety operation and long service life of this machine, please read the operation manual carefully before use the machine. Also please keep the manual in some place easy for your reference. The complete manual includes followed parts:

- Safety Guidance

- Product Overview

- Operation Instruction

- Trouble Shootings

- Technical Annex

- Please kindly understanding that the description of product in this manual might be different from the actual delivered machine due to the continuous improvement of the machine. All improvements and modifications, which are different from this manual, will be without notice. If any difference, the actual delivered product shall prevail.

Safety Notes

Please read the manual before install and operation of this machine.

- Do not reach into the working areas of the running machine.

- Cut off the power supply before maintenance.

- Raise safety awareness and comply the safety operation rules to avoid hazard.

- Please wear personal protection articles as: gloves and safety shoes.

- Do not remove the warning and instruction labels on the machine.

- Make sure the control system meets the state of operation required. Sometimes the set system would change its state. So, please try to make the machine do circle operation slowly till it meets the operation state we expected.

- Do not modify circuits and connections of safety devices. Any modification may result in overvoltage, self-lock, overload and arbitrary power outage. Safety devices are for purpose of protecting both the machine and the operator, modification of them would sabotage their original functions, however.

- This machine only suits for cutting general metal materials, do not cut agriculture and fishery products, wooden materials, food, combustible materials and radioactive metals.

- Keep enough space between machines to avoid hit.

- Do not put any tool on machine, but in toolbox after using. Do not put workpiece or tools in area around the machine to avoid injury.

- Please keep machine clean, remove chips and oil stain from it.

- Never operate machine when its guards are removed.

- Please wear gloves when loading the workpiece, replacing the blade and brush.

- Do not wear gloves when operating the control panel.

- Make sure that the vices clamp the workpiece tightly before feeding.

- Do not opern any door or guard or touch blade when the machine is running.

- Make sure the machine is stopped before replace the saw blade.

When selecting blade, blade speed and coolant, please refer to the operation manual or related documents.

- Content

Chapter 1 FEATURES AND SPECIFICATIONS	5

1.1 Front view	5

1.2 Back view	5

1.2 Back view	6

1.3 CS-330HA Dimension	6

1.3 CS-330HA Dimension	7

Chapter 2 INSTALLATIONS	9

2.1 Machine location	9

2.2 Lifting	10

2.3 Cleaning	10

2.4 Remove the shipping support	10

2.5 Leveling	10

2.6 Hydraulic oil	11

2.7 Cooling water	11

2.8 Cleaning brush	12

2.9 Power supply 50HZ/380v	12

Chapter 3 OPERATION INSTRUCTION	14

3.1 Control board	14

3.2 Machine device description	18

3.3 Blade replacement	19

3.4 Operation instruction	21

Chapter 4 MAINTENACE AND LUBRICATION	26

4.1 Daily maintenance	26

4.2 Weekly maintenance	26

4.3 Half-year maintenance	27

4.4 Yearly maintenance	27

4.5 Lubrication system	27

Chapter 5 BLADE SELECTION	29

5.1 Blade tooth selection	29

5.2 Blade use at the early period	29

5.3 Blade speed and cutting rate selection	29

5.4 Trial running of the blade operation	30

Chapter 6 ACCESSORIES	31

6.1 Chip conveyor	31

6.2 Roller feeder	31

6.3 Over-head clamp vice (optional device)	32

Chapter 7 TROUBLE SHOOTING	34

7.1 Blade problems and solution	34

Chapter 8 RECOMMENDED CUTTING DATA	36

Chapter 9 MAIN WEARING PARTS	37

Chapter 10 TECHNICAL ANNEX	38

10.1 Structure diagram	38

10.2 Gear box	39

10.3 Electric box	40

10.4 Hydraulic principle	41

10.5 Electric diagram	42

# Chapter 1 FEATURES AND SPECIFICATIONS

## 1.1 Front view

## 1.2 Back view

## 1.3 CS-330HA Dimension

1.4 Specifications

| Model | CS-330HA |
| --- | --- |
| Cutting capacity (mm) | Single workpiece | Φ330 W330×H330 |
|  | Bundle cutting | W240×H150 |
| Blade speed（m/min） | 20-70（stepless）or 25,32,42,55,70,80 |
| Blade size（mm） | 4242L×34W×1.1T |
| Blade tension | Hydraulic control |
| Motors（kw） | Blade drive (kw) | 3 |
|  | Hydraulic pump (kw) | 0.75 |
|  | Cooling pump (kw) | 0.06 |
| Oil tank capacity | Hydraulic tank（L） | 40 |
|  | Cooling tank（L） | 35 |
| Machine size（mm） | 2185×1900×1270 |
| Machine weight（kg） | 1500 |

1.5 Pressure settings and values

| Pressure Model | CS-330HA |
| --- | --- |
| Hydraulic system pressure（kg/cm2） | 30+2 |
| Blade tension pressure 100kgs/ cm2（klbs/inch2） | 20±2（28±2） |

# Chapter 2 INSTALLATIONS

## 2.1 Machine location

2.1.1 Plywood case (keep balance of the loading)

2.1.2 Wooden block

## 2.2 Lifting

If travelling overhead crane is used, the slings should be padded to prevent damage of painting.

Make sure the slings are firm; they should be with a lifting capacity 1.5 times of the machine weight. Keep balance and take care of safety.

## 2.3 Cleaning

After the machine has been placed in position, please remove the rust preventive coating using a suitable cleaning solvent (such as kerosene or cleaning agent). Do not use gasoline or corrosive solvent cleaning (guard against fire).

## 2.4 Remove the shipping support

For protecting the saw frame during transportation, there is a support fixing the saw frame to the machine base. After machine positioning, remove this support before using machine. Please keep it in case of relocation of the machine.

## 2.5 Leveling

Place spirit levels on the vise side plates and the work table to adjust the table squareness. Adjust the leveling bolts till the left-and-right (left ±0.1/1000mm) and fore-and-aft (aft ±0.1/1000mm) of the work table leveling. Adjust leveling bolts under machine base to make the machine level. Then check all the leveling bolts are tightened.

Emphasis：For best cutting efficiency, please make the rear of machine 5mm higher after leveling.

## 2.6 Hydraulic oil

Check the oil gauge before using the machine. Oil gauge is installed at left side of machine base obviously. If the oil is not enough, please add DTE24 oil or other similar oil till the oil level is 2 grids higher than the red line of oil gauge.

## 2.7 Cooling water

Before packing, the coolant tank has been drained at factory to keep the tank dry.

Fill cooling water (5~8% saponification liquid, the other is water) into the tank before using. Check the water level on the water gauge to make sure whether there is enough cooling water for machine operating.

After daily working, please clean the machine to prevent from rust; if the machine is left unused for a long period, please apply a coat of oil to it against rust.

IMPORTANT: the cooling pump could not be used when there is no water in the tank, otherwise the cooling pump might be damaged.

## 2.8 Cleaning brush

Incorrect position of the cleaning brush will accelerate wear and tear of saw blade, reduce service life of it and result in noises.

CORRECT                   IMPROPER                INCORRECT

## 2.9 Power supply 50HZ/380v

2.9.1 All power distribution should be made by professional electrical maintenance personnel in accordance to national power distribution standard.

2.9.2 Before power distribution, cut off the power supply in circuit breaker to realize insulation.

2.9.3 Use suitable cable to connect power supply; make sure it agrees with the mechanical voltage value.

2.9.4 After the necessary wiring connections have been done, turn on the circuit breaker. Then check the power is connected correctly.

2.9.5 Turn on the power switch (on the door of electric control box) of machine; the “power light” on operation panel will light up.

IMPORTANT: the blade will stop running as soon as the operator press E-stop button.

2.9.6 Press “hydraulic start” button on operation panel.

IMPORTANT: make sure the shipping support was removed before next step of operating.

2.9.7 Press “frame up” button, the frame will move upward. If it does not action, please check steps from 2.9.8 to 2.9.11 to find out whether the connection of power is correct.

2.9.8 Turn off power switch.

2.9.9 Disconnect the power supply cable.

2.9.10 Interchange any two phase connections.

2.9.11 Do as steps from 2.9.4 to 2.9.7.

# Chapter 3 OPERATION INSTRUCTION

## 3.1 Control board

3.1.1 Operation panel

- PNC control panel

CUTTING QUANTITY—— Machine will action according to the preset data automatically. It will stop till count value the same as the preset value.

CLEAR—— Press this button will clear the count value.

MULTIPLE FEEDING—— Multiple feeding could be set according to requirement. It could feed 9 times at most.

Line speed indicator—— It will indicate the current blade line speed; unit is m/min.

2）E-stop

This button could stop oil pump, water pump and other functions during cutting. Press it again to get rid of the stop state.

3）Power light

When the power switch is turned on after machine has been connected to power supply, this light will light up.

4）Hydraulic start

Press this button will start hydraulic motor.

5）Workpiece feeding forward

At manual work mode, when the front vices are loosen and the back vices are clamped, shuttle feeding device will feed the workpiece forward once press this button. However, if the fast approach bar touched the workpiece, this button couldn’t function.

6）Workpiece feeding backward

At manual work mode, when the front vices are loosen and the back vices are clamped, shuttle feeding device will feed the workpiece backward once press this button. However, if the fast approach bar touched the workpiece, this button couldn’t function.

7）Front vice movement switch

At manual work mode, turn this switch could make the front vice loosen or brief clamp.

8）Feed vices clamp/loosen switch

At manual work mode, turn this switch could make the feed vices loosen or clamp.

9）Front vice clamp

At manual work mode, turn the “Front vice movement switch” to right and don’t let go, press the “Front vice clamp” button at the same time till the indicator (9A) lights up, then the front vice has already clamped the workpiece tightly.

10）Auto/Manual select switch

Turn this switch to left side, machine will be at auto control mode and do continuous cutting.

Turn this switch to right side, machine will be at manual control mode and do single cutting.

11）Blade run button

When the indicator (9A) lights up, press this button, then the main motor and cooling pump will start work as well as the saw frame fast feed downward.

After the fast approach bar touching the workpiece, saw frame will change to do slow feeding downward and the speed was set by operator.

12）Saw frame up button

Press this button and hold it, the main motor will stop and the saw frame will go up. Let go of it, the saw frame will stop.

13）Saw frame down button

Press this button and hold it, the saw frame will fast feed downward.

14）Working light switch

This switch is used to control the working light.

15）Cooling water select switch

Turn this switch to “1” position under manual control mode, the cooling pump starts to work and the cooling water will fluid out. At the same time, the main motor has not worked. Turn the switch to “0” position, the cooling motor will stop

When the saw blade is stop, turn this switch to start the cooling pump could help cleaning chips on machine by the water gun.

16）Blade line speed control knob

This knob is used to adjust the line speed of saw blade.

3.1.2 Hydraulic panel

a. Feed force valve

The feed force valve sets the amount of force applied to push the blade into the workpiece. The feed force setting is indicated by a small indicator arrow on the feed force knob. Please select the feed force according to hardness of workpiece. The numbers from 0 to 10 under the colored chart means the hardness from low to high.

b．Feed rate valve

This valve is under the “Feed force valve”. The operator could adjust the feeding down speed of saw blade by this valve at cutting.

The numbers from 0 to 10 represents the feed rate level.

## 3.2 Machine device description

3.2.1 Movable guide arm

To provide maximum support for the blade, the movable guide arm must always be positioned close to the workpiece but not touch it.

Warning: To avoid damaging the saw, please make sure the guide arm will not strike the workpiece or the front vice.

3.2.2 Fast approach device

The fast approach device locates between the two guide arms. When a cutting cycle is started, the saw frame will feed downward at the set speed before the fast approach device touching the workpiece. After the fast approach device comes into contact with the workpiece, the saw frame will slow to the feed rate set by the feed rate valve.

3.2.3 Hydraulic blade tension

Proper blade tension is applied hydraulically. If need to tension the blade, turn the handle to the “tension” positon as it is showed on the fig. at right side. When the machine is stopped, please turn the handle to the middle (stop) position.

Warning: Do not turn this handle to other positon when the machine is working.

3.2.4 Feed length readout

a．Turn the “Auto/manual select switch ” to “manual” position.

b．Turn the “Feed vice clamp/loosen switch” to clamp position.

c．Press “Workpiece feeding forward” to make the shuttle feeding device move to the forefront.

d．Loosen the retaining screw of handwheel.

e．Rotate the handwheel to make the digit on the readout be the demanded cutting length.

f．Tighten the retaining screw.

3.2.5 Motion detector

This device protects the saw and personnel safety. Once the blade is broken or stallout due to length、strength or pressure of saw blade overload during cutting, this safety device will stop all machine operations automatically.

3.2.6 Shuttle feeding vice

Useful for clamping un-regular shape material.

## 3.3 Blade replacement

a）Turn the “Auto/manual select switch ” to “manual” position.

b） Press “Hydraulic star” button.

c） Press “saw frame up button” to drive the saw frame move upward till the end of right guide arm a little higher than the front vice.

d）Open the saw wheel covers.

Warning: To avoid injury, be sure to securely support both covers with their stays.

e）Back off the carbide inserts set screws.

f）Descent the chip brush.

g）Turn the hydraulic blade tension handle to loosen position. The driven wheel moves toward the drive wheel and release blade tension. When the blade could be taken out, turn the blade tension handle to the stop position and replace the saw blade.

h）Remove the used blade.

i） Place a new blade onto the saw wheels. Insert the saw blade into both left and right inserts and into both auxiliary bearings at end of guide arms. The blade teeth must face down.

Note: please wear gloves for safety.

j）Turn the blade tension handle to tension properly to make the blade tighten a little.

k）Make the back of saw blade to the convex edges of saw wheels as close as possible. Turn the blade tension to tension position and the saw blade will be tightened.

i）Lock the carbide inserts set screws by hand, and turn back round 1/4 circle

m）Restore the brush assembly. Make it touch the root of the saw blade teeth.

n）Close the wheel covers.

## 3.4 Operation instruction

3.4.1 Manual work

（1）Select suitable blade according to material、size and shape of the workpiece.

（2）Equip the saw blade.

（3）Adjust the movable guide arm to proper position according to size of workpiece.

（4）Load the workpiece onto the feeder table:

a ) Turn the “Auto/manual select switch ” to “manual” position.

b ) Press “saw frame up button” to drive the saw frame move upward till saw blade is higher than the front vice.

c ) Open the front and back vices to proper width.

d ) Place the workpiece between the back vices and make it about 150mm beyond front side of back vices.

（5）Adjust the blade speed

a ) Turn the “Feed rate valve” to 0.

b ) Turn the “Auto/manual select switch ” to “manual” position.

c ) Turn the “Front vice movement switch” to right (clamp) and don’t let go, press the “Front vice clamp” button at the same time till the indicator (front vice clamp) lights up.

d ) Press “Blade run button”.

e ) Turn the blade line speed control knob to select a proper line speed according to material of workpiece.

f ) Adjust the line speed according to size and shape of workpiece.

Note: To ensure the service life of the saw blade, there must be a run-in time for a new blade.

（6）Cut off the scrapped part.

a ) Turn the “Auto/manual select switch ” to “manual” position.

b ) Feed vice clamp the workpiece while the front vice loosen.

c ) Press “Workpiece feeding forward” to feed the workpiece forward.

d ) Front vices clamp the workpiece while the feed vice loosen.

e ) Press “Workpiece feeding backward” to make the shuttle vices move backward.

f ) Repeat motions from “a” to “e” to make the workpiece proper length beyond the saw blade.

Note: Please note that the fast approach device should not touch the workpiece when adjusting the cutting length. Otherwise the shuttle feed vices will not work.

g ) Turn the “Front vice movement switch” to right (clamp) and don’t let go, press the “Front vice clamp” button at the same time till the indicator (front vice clamp) lights up.

h ) Press “Blade run button” to start cutting. It will stop automatically after cutting.

Note: Before press “blade run button”, please make sure all covers are closed and your body or items on your body not touching saw blade.

（7）Set the cutting length:

a ) Firstly, do the steps of “Cut off the scrapped part”.

b ) Front vices clamp the workpiece while the feed vices loosen.

c ) Press “Workpiece feeding forward” to move the shuttle feed vices to front end.

d ) Set the cutting length by the “Feed length readout”. (Refer to step 3.2.4)

e ) Loosen the front vices and feed vices.

f ) Press “Workpiece feeding backward” to make the shuttle feed vices back to set cutting length.

g ) Press “Workpiece feeding forward” to move the shuttle feed vices to front end.

h ) Turn the “Front vice movement switch” to right (clamp) and don’t let go, press the “Front vice clamp” button at the same time till the indicator (front vice clamp) lights up.

i ) Press “Blade run button” to start cutting. It will stop automatically after cutting.

Note: If the cutting length is longer than the feeding stroke, repeat steps from “e” to “h”. In this case, the method for set the cutting length is to set 1/n at the “Feed length readout”, “n” means the feeding times.

Note: The chip shape could help to know the whether the feed rate and blade line speed are correct. Refer to figs. below:

3.4.2 Automatic work.

      - Cut off the scrapped parts by the steps mentioned in operation of“manual work”.

      - Turn the “Auto/manual select switch ” to “manual” position.

      - Press “saw frame up button” to drive the saw frame move upward till end of fast approach device is 10mm higher than the workpiece.

      - Press “Workpiece feeding forward” to move the shuttle feed vices to front end.

      - Set cutting length by the “Feed length readout”. Please refer to step (6) in operation of “manual work”.

      - Turn “Front vice movement switch” to front vice clamp, loosen feed vices.

      - Press “Workpiece feeding backward” to make the shuttle feed vices back to the end.

      - Feed vices clamp the workpiece.

      - Press “Workpiece feeding forward” to feed the workpiece to front end.

      - Turn the “Front vice movement switch” to right (clamp) and don’t let go, press the “Front vice clamp” button at the same time till the indicator (front vice clamp) lights up.

      - Set the cutting quantity.

- Input the cutting quantity at “PRESET”.

- Press “CLEAR” to clear the data in “COUNT” area.

      - Turn the “Auto/manual select switch ” to “auto” position, and press “blade run button”. The shuttle feed vices will move backward and clamp. The saw frame start to feed downward.

      - When the set quantity is finished (the value in COUNT area is the same with PRESET area), the machine will stop automatically and the saw frame stop at the  down positon.

Note:

  - During auto cutting, if turn the “Auto/manual select switch ” to manual position, the saw frame will stop after finishing the current cutting and stop at the down position.

  - During cutting, if press “Saw frame up button”, the saw blade will stop and the saw frame move upward.

After finishing the auto cutting task, if you start another auto task, please turn the “Auto/manual select switch ” to “manual” position and do steps from (10) to (12)  mentioned above.

# Chapter 4 MAINTENACE AND LUBRICATION

Cleaning all the excess chips after working. After clean the bandsaw, descend the saw frame to the lowest place. Press the e-stop button and cut off the power supply.

## 4.1 Daily maintenance

Follow the steps before operating the machine：

- Check the hydraulic oil gauge to find if the oil level pass the red line L, when the oil below the red line, add the hydraulic oil.

- Check the coolant water gauge to find if the level pad the red line L. When it’s below, add cooling water.

- Check if the saw blade one the left-and-right blade wheel and inserted into the front-and-rear carbides.

- Check whether the brush is at proper position.

## 4.2 Weekly maintenance

- Add proper grease at positions as follows:

  - Idle wheel

  - Connecting rod bearing seat of the brush. (2pcs)

  - Idle wheel blade tension seat.

  - Worm bearing seat of gear box. (2pcs)

## 4.3 Half-year maintenance

Replace gear oil.

Gear oil type： n°140

Attn.: new machinery must replace the gear oil after using 600 work hours or three months. Then replace it per 1200 work hours or six months

## 4.4 Yearly maintenance

Replace hydraulic oil

Hydraulic oil type:ISO-VG Grade n°32

## 4.5 Lubrication system

| No. | Lubricate part | Method | Time | Quantity | Recommend oil | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Gear oil tank | Add oil: open fill cap and fill with oil until you see the oil level reach the halfway point. Discharge oil: open the oil venting spile | Per six months | 30L | L-CKC150 gear oil |  |
| 2 | Hydraulic oil tank |  | Per six months | 75L | L-HL32 Mineral oil Type hydraulic oil |  |
| 3 | Column | Saw frame upand down, press the manual pump | Per week | 0.5L | N32～N68 machine oil |  |
| 4 | Linear guide surface of the assistance column | Top end of the assistance column (close to the assistance lift cylinder) | Per month | suitable | High quality oil |  |
| 5 | Linear guide surface | Oil the tooth rank | Per month |  |  |  |
| 6 | Oil orifice of the gear box | Use oil gun | Per month | 2 PCS | Mobil- EPL grade： NLGIL | Forbid to use other brand oil, user assume sole responsibility for bearing damage cause by this |
| 7 | Shaft of the idle wheel |  | Per month | 1 PC |  |  |
| 8 | Blade brush bearing seat |  | Per month | 2 PCS |  |  |
| 9 | Blade tension guide slide |  | Per month | 2 PCS | High quality oil |  |
| 10 | Chain of the chip conveyor slot |  | Per month | suitable |  |  |
| 11 | Coolant water tank | Use the barrel or basin cool water and coolant liquid | Every day accordig to the need | capacity：280L | YRA or YRB emulsion，mix with water | Discharge and clean the transmutative coolant water, fill new one |
| 12 | Parts without paint | Brush | According to the need | Suitable | N32～N68 machine oil | Avoid rust, keep appearance and ensure the performance |

# Chapter 5 BLADE SELECTION

## 5.1 Blade tooth selection

a）Solid material ---- 2/3T    3/4T

b）Hollow material ---- 3/4T   4/6T

c）High rigidity, toughness material ---- 2/3T

d）Thin maerial ---- 4/6T  5/8T

e）Big size of shape steel ---- 3/4T;  the vice press: 8 – 12 kgs

## 5.2 Blade use at the early period

When use the new blade, choose the cutting speed accord to the material.

E.G.: Steel 45#, dia.200mm, fist cut, adjust the feeding speed as the 20% of the normal; second cut, adjust at 50%, third cut, normal feeding speed. Adjust accord the rigidity of the material. Otherwise, it will affect the blade efficiency, short the blade service life.

The advantage of correct use the blade at the early period:

● long blade service life；

● fast cutting speed；

● higher cutting efficiency

## 5.3 Blade speed and cutting rate selection

select the suitable blade speed and cutting rate according to the workpiece.

Cute rate (m2/m) = size of the material (m2)/cut time (m/min)

After blade speed selected, adjust the “flux adjust switch’ on the control panel, make the saw frame has a suitable feeding speed, and cutoff the workpiece with suitable time.

（Bi-Metal M42）

| Material JIS mark | Blade speed（m/min） | Cutting rate（cm2/min） |
| --- | --- | --- |
| SS41 | 45-70 | 35-45 |
| S45C | 45-70 | 40-50 |
| SNCM439(SNCM8) | 40-50 | 23-30 |
| SNCM220(SNCM21) | 40-55 | 25-32 |
| SCM440(SCM4) | 40-55 | 25-32 |
| SCM415(SCM21) | 45-60 | 28-35 |
| SKS | 35-50 | 25-32 |
| SKD1 | 20-30 | 10-15 |
| SKD11 | 20-30 | 12-18 |
| SKD61 | 25-35 | 15-22 |
| SUS304 | 20-30 | 15-20 |
| SUS316 | 20-30 | 10-15 |

## 5.4 Trial running of the blade operation

Before we use a new blade, do the trial running first. Failure trial running will short the blade service life and reduce the work efficiency.

New blade      Correct install and use   Un-correct install and use

Advantage of correct cutting：

＊prolong blade service life

＊increase cutting speed

＊improve cutting veracity

＊reduce blade change rate

# Chapter 6 ACCESSORIES

## 6.1 Chip conveyor

Chip conveyor will discharge the chips automatically.

## 6.2 Roller feeder

Equip rear side of the machinery, used for feeding workpiece with long length.

## 6.3 Over-head clamp vice (optional device)

This device used for bundle cutting purpose.

Bundle cutting work process:

6.3.1 Screw the device on the vice

6.3.2 Adjust the adjusting screw rod to proper height (the distance between treadle bar and bundle workpiece is about 6~10mm), loosen the screw and make the treadle bar proper width (make sure it can clamp every workpiece).

6.3.3 Equip the material support vice (1) on the support table. This device used for avoid the material fall down form the table.

6.3.4 Manual operation please refer to 3.4.1

Automatic operation please refer to 3.4.2

6.3.5 Bundle cutting capacity

Max. cutting width：150mm  to  240mm

Max. cutting height：50mm   to  150mm

6.3.6 Material condition at bundle cutting.

# Chapter 7 TROUBLE SHOOTING

## 7.1 Blade problems and solution

Shake

Bad cuts

Blade cannot lift

Cuts are crooked

Blade break

| Symptom | Possible cause | Corrective action |
| --- | --- | --- |
|  | ● | ● | ● |  | lack of coolant water | Add to appointed level |
| ● |  | ● | ● |  | there is air in cylinder | Let the air out |
| ● | ● | ● | ● | ● | unsuitable blade | Charge blade |
| ● | ● | ● | ● | ● | excessive change voltage | Fix the voltage |
| ● |  | ● | ● |  | left guide arm too far away form the work piece | Get the arm close to the work piece but not touch |
| ● |  | ● | ● | ● | too tighten of the guide arm | adjustment |
|  |  | ● |  | ● | blue or purple chips | descend feed rate |
| ● |  | ● |  | ● | Chips stack in the guide plate | clean |
| ● | ● | ● | ● | ● | Up guide plate abrasion or shatter | replace |
| ● |  |  | ● |  | Blade unsuitable touch up guide plate | Adjust the distance |
| ● |  | ● | ● |  | Work piece unsuitable place | Re-rank |
| ● |  | ● |  | ● | Blade edge touch the active & idle wheel | Obligate suitable gap |
| ● | ● | ● |  |  | un-smooth surface of the material | Smooth the surface |
| ● | ● | ● | ● |  | Blade TPI shatter | Replace blade |
| ● |  | ● | ● |  | excessive cutting pressure | Reduce the press |

Shake

Bad cuts

Blade cannot lift

Cuts are crooked

Blade break

| Symptom | Possible cause | Corrective action |
| --- | --- | --- |
| ● | ● |  |  |  | low cutting pressure | Increase press |
| ● | ● | ● | ● | ● | blade TPI wrong choose | Change blade |
| ● | ● | ● | ● | ● | blade stop run | re-start blade motor |
| ● |  | ● | ● | ● | excessive cutting speed | reduce blade speed |
| ● | ● | ● | ● |  | slow cutting speed | increase blade speed |
| ● |  | ● | ● | ● | excessive blade feeding speed | reduce speed |
| ● | ● |  |  |  | slow blade feeding speed | Increase speed |
| ● |  | ● | ● |  | Low blade tension | Increase tension press |
| ● |  | ● | ● | ● | un-correct steel brush position | Adjust the position or replace |
| ● |  | ● | ● |  | Guide plate un-correct clamp the blade | Check and modify |
| ● | ● | ● | ● | ● | un-correct clamp work piece | re-clamp |
| ● | ● | ● | ● |  | Too rigidity surface of the work piece | Intenerate surface |
|  | ● | ● |  |  | Work piece without anneal | Change to a anneal one |
| ● |  | ● | ● | ● | Lack or degenerative of the cutting liquid | Add or replace the liquid |
| ● |  | ● | ● | ● | Shake cause by the close to other machinery | Prevent shake or reassembly machinery |

# Chapter 8 RECOMMENDED CUTTING DATA

| material | Steel mark | Saw blade speed （m/min） | Cutting Rate（cm2/min） |
| --- | --- | --- | --- |
|  | GB （China） | JIS （Japan） | AISI (US) | DIN （Germany） |  |  |
| Low carbon steel | 08 | S10C | 1010 | C10 | 50-75 | 70-80 |
|  | 15 | S15C | 1015 | C15 | 50-75 | 70-80 |
| Middle carbon steel | 45 | S45C | 1045 | C45 | 50-70 | 60-70 |
|  | 55 | S55C | 1055 | CK55 | 50-70 | 50-60 |
| Carbon tool steel | T10 | SK4 | W1 | C75W | 40-50 | 25-45 |
|  | T12 | SK2 | W1 | C125W | 40-50 | 35-45 |
|  | T8Mn | SK2 | W1 | C125W | 40-50 | 35-45 |
| Alloy structure steel | 40CrNi | SNC236 | 3140 | 40NiCr6 | 30-40 | 30-40 |
|  | 40CrMoA | SCM440 | 4140 | 42CrMo8 | 40-50 | 35-45 |
|  | 40CrNiMoA | SNCM439 | 4340 | 34CrNiMo8 | 35-45 | 30-40 |
| High speed steel | W18Cr4V | SKH2 | T1 | S18-0-1 | 25-35 | 20-30 |
|  | W18Cr4VCo5 | SKH3 | T4 | S18-1-2-5 | 20-30 | 15-25 |
| Cold mould alloy tool steel | Cr12MoV | SKD11 | D2 | X155CrVMo121 | 25-35 | 20-25 |
|  | CrWMn | SKS2 | D7 | 105WCr6 | 20-30 | 15-20 |
|  | 9SiCr | SKS3 | D1 | 105WCr6 | 25-35 | 20-25 |
| Heat mould alloy tool steel | 3Cr2W8V | SKD5 | H21 | X30CrV93 | 35-45 | 30-35 |
|  | 4Cr5MoV1Si | SKD61 | H13 | X40CrMoV51 | 30-40 | 25-30 |
|  | 5CrNiMo | SKT4 | L6 | X55NiCrMoV6 | 25-30 | 20-25 |
| Alloy spring steel | 50CrVA | SUP10 | 6150 | 50CrV4 | 20-35 | 25-35 |
|  | 50CrMnVA | SUP10 | 6150 | 50CrV4 | 20-35 | 25-35 |
| Bearing steel | GCr15 | SUJ2 | 52100 | 100Cr6 | 35-45 | 30-40 |
| Stainless steel | Ocr18Ni9 | SUS304 | 304 | X5CrNi1810 | 35-45 | 20-30 |
|  | oCr17Ni12Mo2 | SU316 | 316 | X5CrNiMo1712 | 20-25 | 15-20 |
|  | 1Cr17 | SU430 | 430 | X6Cr17 | 30-40 | 25-35 |

# Chapter 9 MAIN WEARING PARTS

| No. | Name | Mark | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Brush | 5ST-9010 | 1 |  |
| 2 | Top guide carbide | K01121700 | 2 |  |
| 3 | Left front guide carbide | K01121800 | 1 |  |
| 4 | Left rear guide carbide | K01121900 | 1 |  |
| 5 | Right front guide carbide | K01122000 | 1 |  |
| 6 | Right rear guide carbide | K01122100 | 1 |  |

# Chapter 10 TECHNICAL ANNEX

## 10.1 Structure diagram

## 10.2 Gear box

## 10.3 Electric box

## 10.4 Hydraulic principle

## 10.5 Electric diagram